## KOMATSU  EXCAVATOR

## PC750-6

### LOADING  SHOVEL

| WITH: | MIKUNI HEATER, |
| --- | --- |
|  | 4.5 m3 BOTTOM DUMP BUCKET, |
|  | 4600 mm BOOM & 3400 mm ARM, |
|  | STEEL CAB |
|  | 610 mm DOUBLE GROUSE SHOE |
| FOR: | -40oC to +40oC OPERATION |

(Specification are subject to change without notification)

KOMATSU PC750-6 HYDRAULIC EXCAVATOR

(LOADING SHOVEL)

| SPECIFICATIONS |
| --- |
| OPERATING WEIGHT |  |
| With 4.5 m3 (5.89 cu. Yd) bucket 74,680 kg |
| INCLUDING LUBRICANT, FULL FUEL TANK, HYDRAULIC OIL, OPERATOR, AND Boom : 4600 mm One-piece Arm : 3400 mm Bucket : Heaped 4.5 m3 Bottom dump Shoe : 610 mm Double |
| FLYWHEEL HORSEPOWER: |  |
| SAE (J1349) | 444 HP (331 kW) / 1800 RPM |
| DIN (6270) | 450 PS (331 kW) / 1800 RPM |
| BUCKET CAPACITY |  |
| Heaped | 4.5 m3 |
| Struck | 3.60 m3 |
| BUCKET WIDTH | 2320 mm |
| BOOM LENGTH | 4600 mm |
| ARM LENNGTH | 3400 mm |
| DIGGING FORCE |  |
| Bucket digging force |  |
| With 3.80 m3 bucket | 44,000 kgf (97,000 lb / 431 kN) |
| With 4.50 m3 bucket | 40,800 kgf (89,950 lb/ 400 kN) |
| ARM CROWD FORCE | 45,000 kgf (99,210 lb / 441 kN) |
| ENGINE: |  |
| MANUFACTURER | KOMATSU |
| MODEL | SAA6D140E-2 |
| COOLING SYSTEM | WATER COOLED |
| ASPIRATION | TURBOCHARGED AND AFTERCOOLED |
| No. OF CYLINDERS | 6 |
| BORE | 140 mm |
| STROKE | 165 mm |
| PISTON DISPLACEMENT | 15.24 ltr. |
| Performance: |  |
| Max. torque | 2099 N.m (214 kgf.m) |
| Engine RPM at max. torque | 1350 RPM |
| FUEL SYSTEM |  |
| FUEL | DIESEL GAS OIL, ASTM SPECIFICATION D975-60T No. 2D |
| COMBUSTION METHOD | DIRECT INJECTION |
| GOVERNOR TYPE | MECHANICAL, ALL-SPEED CONTROL |
| LUBRICATION SYSTEM: |  |
| LUBRICATION METHOD | FORCED LUBRICATION |
| LUBRICATION PUMP | GEAR PUMP |
| LUBRICATION FILTER | FULL-FLOW and bypass combination |
| COOLING METHOD | WATER COOLED |
| FAN TYPE | SUCTION TYPE |
| AIR CLEANER TYPE | DRY TYPE WITH AUTOMATIC DUST EVACUATOR |
| STARTING SYSTEM: |  |
| STARTING METHOD | BY ELECTRIC MOTOR |
| STARTING MOTOR VOLTAGE | 24 V |
| STARTING capacity | 11.0 kW |
| ALTERNATOR VOLTAGE | 24 V |
| ALTERNATOR AMPERAGE | 75 A |
| BATTERY | 2 x 12 V / 170 Ah |
| HYDRAULIC SYSTEM: |
| Type | OLSS (Open-center Load Sensing hydraulic system) |
| No. of selectable mode | 2 |
| MAIN PUMP |  |
| TYPE | VARIABLE CAPACITY PISTON PUMP |
| No. OF PUMP | 2 |
| MAXIMUM FLOW | 1015 ltr./min. |
| SUB pump |  |
| Type | Gear pump |
| Maximum flow | 140 ltr./min. |
| RELIEF VALVE SETTINGS |  |
| IMPLEMENT CIRCUITS | 320 kg/cm2 |
| TRAVEL CIRCUITS | 320 kg/cm2 |
| SWING CIRCUITS | 290 kg/cm2 |
| PILOT CIRCUITS | 30 kg/cm2 |
| CONTROL VALVE |  |
| TYPE | 1-spool type x 1 4- spool type x 1 5-spool type x 1 |
| HYDRAULIC MOTOR |  |
| TRAVEL | AXIAL PISTON TYPE x 2 |
| SWING | AXIAL PISTON TYPE x 1 |
| No. of cylinders-bore x stroke x rod dia. |  |
| BOOM | 2-180 mm x 1490 mm x 120 mm |
| ARM | 1- 225 mm x 1530 mm x 160 mm |
| BUCKET | 2- 180 mm x 1300 mm x 130 mm |
| Bucket bottom | 2- 140 mm x 335 mm x 90 mm |
| OPERATOR’S CAB: |  |
| TYPE | ALL WEATHER, ENCLOSED TYPE |
| IMPLEMENT CONTROLS: |  |
| TYPE | TWO LEVERS ACTUATED BOOM, ARM, BUCKET AND SWING |
| STEERING CONTROL: |  |
| TYPE | Two-lever with pedal |
| DRIVE: |  |
| DRIVE METHOD | HYDROSTATIC |
| REDUCTION SYSTEM | 3-stage planetary gear |
| MAXIMUM DRAWBAR PULL | 57,000 kgf (559 kN) |
| MAXIMUM TRAVEL SPEED (High) | 4.2 km/h |
| Maximum travel speed (Low) | 2.7 km/h |
| Gradeability | 70% (35 deg) |
| BRAKE: |  |
| TRAVEL |  |
| SERVICE BRAKE | HYDRAULIC LOCK |
| PARKING BRAKE | Wet, multiple-disk brake |
| SWING |  |
| SERVICE BRAKE | HYDRAULIC LOCK |
| PARKING BRAKE | Wet, multiple-disk brake |
| UNDERCARRIAGE |  |
| TYPE | CRAWLER-TRACTOR-DESIGN UNDERCARRIAGE |
| CENTER FRAME | H – leg frame |
| SEAL OF TRACK | SEALED TRACK |
| TRACK ADJUSTER | HYDRAULIC TYPE |
| ROLLER TYPE | FLOATING SEAL |
| TRACK SHOES |  |
| TYPE | Double |
| No. OF SHOES | 47 each side |
| No. OF ROLLERS |  |
| CARRIER ROLLERS | 3, each side |
| TRACK ROLLERS | 8, each side |
| GROUND PRESSURE | 1.21 kg/sm2 (119 kPa) |
| SWING SYSTEM |  |
| DRIVE METHOD | HYDROSTATIC |
| REDUCTION SYSTEM | Planetary gear, double-reduction |
| SWING CIRCLE BEARING | Single row shear type ball bearing |
| SWING SPEED | 5.7 RPM |
| SERVICE REFILL CAPACITIES: |  |
| FUEL TANK | 880.0 ltr. |
| RADIATOR | 85.0 ltr. |
| ENGINE | 32.0 ltr. |
| FINAL DRIVE, EACH SIDE | 20.0 ltr. |
| SWING DRIVE | 30.0 ltr |
| HYDRAULIC SYSTEM | 440.0 ltr. |

(Specification are subject to change without notification)

KOMATSU PC750-6  HYDRAULIC EXCAVATOR

(LOADING SHOVEL)

DIMENSIONS

| (BOOM 4600 mm, ARM 3400 mm) |
| --- |
| A:OVERALL LENGTH | 9760 mm |
| B:OVERALL WIDTH | 4110 mm |
| C:OVERALL HEIGHT (TO TOP OF BOOM) | 5075 mm |
| D:OVERALL HEIGHT (TO TOP OF CAB) | 3515 mm |
| E:GROUND CLEARANCE, COUNTERWEIGHT | 1555 mm |
| F:MIN. GROUND CLEARANCE | 840 mm |
| G:TAIL SWING RADIUS | 4300 mm |
| H:LENGTH OF TRACK ON GROUND | 4500 mm |
| I:TRACK LENGTH | 5810 mm |
| J:TRACK GAUGE | 3500 mm |
| K:WIDTH OF CRAWLER | 4110 mm |
| K: Width of crawler (when retracted) | 3390 mm |
| L:SHOE WIDTH | 610 mm |
| M:GROUSER HEIGHT | 50 mm |
| N:MACHINE HOOD HEIGHT | 3495 mm |
| O:MACHINE COUNTER WEIGHT HEIGHT | 2965 mm |
| P:MACHINE CAB WIDTH | 3195 mm |
| Q: Distance, swing center to rear end | 4205 mm |

KOMATSU PC750-6  HYDRAULIC EXCAVATOR

(LOADING SHOVEL)

| WORKING RANGE with 4.5 m3 bucket |
| --- |
| 4600 mm BOOM |
| 3400 mm ARM |
| A: MAX. CUTTING HEIGHT | 10765 mm |
| B: MAX. DUMPING HEIGHT | 7630 mm |
| C: MAX. DIGGING DEPTH | 3515 mm |
| D: MAX.DIGGING REACH | 10095 mm |
| E: MAX.DIGGING REACH AT GROUND LEVEL | 9720 mm |
| F: LEVEL CROWDING DISTANCE | 3970 mm |
| G:REACH AT MAX.DUMPING HEIGHT | 5550 mm |
| H: MIN. SWING RADIUS | 5805 mm |
| I: MAX. HEIGHT OF MIN. SWING RADIUS | 7005 mm |

KOMATSU PC750-6  HYDRAULIC EXCAVATOR

(LOADING SHOVEL)

ACCESSORY PARTS TABLE

| PART No. | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
|  | STARTING SWITCH KEY | 2 |  |
|  | PARTS BOOK | 1 |  |
|  | OPERATION & MAINTANANCE MANUAL | 1 |  |

KOMATSU 750-6  HYDRAULIC EXCAVATOR

(LOADING SHOVEL)

OPTIONAL TOOL TABLE

| PART No. | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
| 09000-30006 | WRENCH SET | 1 |  |
| 09020-10284 | SOCKET WRENCH SET | 1 s |  |
| 09033-00190 | SCREWDRIVER | 1 |  |
| 09036-00150 | PLIERS | 1 |  |
| 09039-00150 | SCREWDRIVER | 1 |  |
| 09055-10390 | BAR | 1 |  |
| 09019-08035 | WRENCH | 1 | FOR FILTER |
| 178-98-11120 | WRENCH | 1 |  |
| 195-98-11590 | SOCKET | 1 |  |
| 07950-80002 | GREAE PUMP | 1 |  |
| 07950-90403 | CARTRIDGE (GREASE) | 1 |  |
| 07951-11400 | NOZZLE | 1 |  |
| 09056-05513 | TOOL BAG | 1 |  |

KOMATSU PC750-6  HYDRAULIC EXCAVATOR

(LOADING SHOVEL)

SPARE PARTS TABLE

| PART No. | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
| 600-211-1231 | CARTRIDGE | 2 | ENGINE OIL FULL-FLOW FILTER |
| 600-212-1511 | CARTRIDGE | 1 | ENGINE OIL BYPASS FILTER |
| 600-311-7132 | CERTRIDGE | 2 | FUEL FILTER |
| 6128-81-7042 | ELEMENT ASS'Y | 1 | AIR CLEANER |
| 6212-85-6840 | V-BELT | 1 | FOR ALTERNATOR DRIVE |
| 600-736-9650 | V-BELT | 1 | FOR FAN DRIVE |
| 07063-01210 | ELEMENT | 2 | FOR HYDRAULIC OIL RETURN FILTER |
| 07000-05180 | 0-RING | 2 | FOR HYDRAULIC OIL RETURN FILTER |
| 363-60-33310 | FILTER | 1 | FOR HYDRAULIC DRAIN FILTER |
| 07002-03034 | O-RING | 4 | FOR FINAL DRIVE DRAIN PLUG |
| 07002-32434 | 0-RING | 1 | FOR P.T.O. DRAIN PLUG |