КОМАTSU BULLDOZER

D375A-5

With SEMI-U TILT DOZER

GIANT RIPPER

STEEL CAB & ROPS CANOPY

710 mm SINGLE GROUSER SHOE

AIR CONDITIONER

SANDY AREA ARRANGEMENT

FOR –20C  - +40C OPERATION

KOMATSU D375A-5 TRACTOR

Specifications

OPERATING WEIGHT 	49800 kg (109,790 Ib.)

FLYWHEEL HORSEPOWER;

SAE (J1349) 	391 kW (525 HP) /1800 rpm

DIN (6270) 	391 kW (532 PS) /1800 rpm

PERFORMANCE:

Travel speed and drawbar pull:

Forward 1st 	0 -  3.8 km/h (2.4	MPH)

2nd 	0 -  6.8 km/h (4.2	MPH)

3rd 	0 - 11.8 km/h (7.3	MPH)

Reverse 1st 	0 -  5.1 km/h (3.2	MPH)

2nd 	0 -  9.2 km/h (5.7	MPH)

3rd 	0 - 15.8 km/h (9.8	МНР)

Max. drawbar pull: 	Refer to attached travel

performance curve
Turning radius 	4.2 m (13 ' 9")

DIMENSIONS:

Overall length	5770 mm (1841")

Overall width	3220 mm (10'7")

Overa11 he ight:

To top of exhaust pipe	4035 mm (13'3")

Highest point,

exclusive of exhaust pipe .... 3429 mm (11'3")

To top of precleaner

Track gauge	2500 mm ( 8'2")

Length of track on ground 	3840 mm (12'7")

Ground pressure 	 123 kPa

(1.25 kgf/cm2/17.8 PSI)
Ground clearance 	  610 mm ( 2' 0"}

ENGINE:

Model  	 Komatsu SA6D170E-3

Type   	 Water cooled, 4-cycle,

overhead valve, direct injection, turbocharged diesel engine with aftercooler

No. of cylinders - bore x stroke .... 6 - 170 mm x 170 mm

(6.69м х 6.69")

Piston  displacement   	23.15   Itr.    (1,413   in3}

Performance:

Max.    torque	2648  N.m

(270  kgf.m/1,953   Ib.ft)

Engine  rpm at max.   torque   	1300   rpm

Fuel   system:

Fuel   	Diesel gas oil,   ASTM

Specification D975-60T No.2D
Governor  type   	Electronic,   all-speed control

SPEC.  NO.  X21SP20010012

D375-lm

Lubrication system:

Lubrication method 	 Gear pump, forced lubrication

Lubrication filter 	 Full-flow

Cooling method 	 Water cooled

Cooling system:

Cooling method 	 Forced circulation by

centrifugal water pump
Fan type 	 Pusher type fan

Air cleaner	 Dry type with dust indicator

and pre-cleaner with automatic dust ejector

Starting system:

Starting method 	 By electric starting motor

Starting motor	 24 V, 2 x 7.5 kW

Alternator 	 24 V, 60A

Battery 	 24 V (12 V x 2) - 170 Ah

POWER TRANSMITTING SYSTEM:

Torque converter:

Type	 3-element, single-stage,

single-phase with lockup clutch

Cooling method	 Water cooled

TRANSMISSION:

Type 	 Planetary gear and multiple-
disc clutch, hydraulically
actuated, forced lubrication

Gear shift 	 3 forward and 3 reverse speeds

Bevel gear	 Spiral bevel gear, splash

lubrication

Steering system:

Steering clutch	 Wet, multiple-disc clutch,

Spring loaded, hydraulically released, hand operated, interconnected with steering brake

Steering brake	,	 Wet, multiple-disc,

spring actuated, hydraulically released, foot/lever operated

Service brake ,	,	 Steering brakes function as

service brake, foot operated

Final drive	 Spur gear single reduction

and planetary gear single reduction, splash lubrication

UNDERCARRIAGE:

Suspension 	 Oscillation type, equalizer bar

SPEC. NO. X21SP20010012 D375-2m

No of rollers:

Carrier rollers ................ 2, each side

Track rollers  	7, each side

Track shoe assembly:

Type	Assembled, lubricated and

sealed track

Pitch 	280mm (11.0")

Track shoe:

Type                    Single grouser (Extreme service)

Grouser height	93 mm. ( 3.7")

Shoe width	710 mm (28")

SERVICE REFILL CAPACITIES:

Specified        Refilled

Coolant	     165 ltr.	165 ltr.

{ 43.6 U.S. gal)  ( 43.6 U.S. gal)

Fuel tank 	     1050 ltr.        1050 ltr.

( 277 U.S. gal)   ( 277 U.S. gal)

Engine	      	68 ltr.          55.5 ltr.

(	18.0 U.S. gal)	 ( 14.7 U.S. gal)

Damper		      2.1 ltr.         2.1 ltr.

(	0.6 U.S. gal)	  ( 0.6 U.S. gal)

Torque converter)		275 ltr.	150 ltr.

Transmission   )                (  72.7 U.S. gal)	( 39.6 U.S. gal)

Bevel gear case )

Steering case  )

Final drive case, each side . .     	65 ltr.           65 ltr.

(	17.1 U.S. gal)	( 17.1 U.S. gal)

SPEC. NO. X21SP20010012

D375-3m

SPEC. NO. X21SP20010012

D375-4m

SPEC. NO. X21SP20010012

D375-5m

SPEC. NO. X21SP20010012

D375-6m

KOMATSU D375A-5 SEMI-U-DOZER

Specifications

EQUIPMENT WEIGHT (Additional weight to tractor):

Standard blade 	10540 kg (23,240 Ib. )

With weld-on push plate 	11140kg (24,5601b.)

DIMENSION:

Length

(Additional length to tractor) .. 1865 mm { 6' 1")

Overall width	 4695 mm (15 '5")

Ground pressure (Additional pressure to tractor):

Standard blade 	 21.6 kPa 0.22 kgf/cm2/3.13 PSI)

With weld-on push plate 	 23.5 kPa 0.24 kgf/cm2/3.13 PSI}

DOZER EQUIPMENT:

Type 	 Semi-U blade, hydraulically

tilting

Weight:

Standard blade 	 10490 kg (22,130 Ib)

With weld-on push plate 	11090 kg (24,450 Ib)

Including blade support 930 kg (2,050 Ib) Blade:

Blade capacity 	18.5 m3 (24.2 yd3)

Blade support method 	Brace support type

Width 	4695mm (15’ 5")

Height 	2265 mm ( 7’ 5")

Digging angle	55 deg.

Max. lift above ground 	1660 mm ( 5’ 5")

Max. drop below ground 	 715 mm ( 2’ 4")

Max. tilt adjustment 	1065 mm ( 3’ 6")

Hydraulic cylinders:

Type .	 Double-acting, piston type

No. of cylinders - bore:

Lifting cylinder 	 2 - 150 mm (5.9")

Tilting cylinder 	 1 - 225 mm (8.9")

HYDRAULIC EQUIPMENT:

Additional hydraulic oil weight ... 50 kg (110 Ib)

Max. oil pressure 	 20.6 MPa (210 kgf/cm2, 990 PSI)

Hydraulic pump:

Type	  Gear pump

Capacity (discharge flow) 	 405 Itr. (107 U.S. gal)/min

at engine rated rpm

Location 	 Rear of engine right side

Control valve 	 Spool type

Position:

Lifting spool 	 Raise, hold, lower and float

Tilting spool 	 Right, hold and left

Hydraulic tank:

type	 Equipped with externally-
mounted control valve

Location 	,	 Right of operator's seat

filter 	 Full-flow type

Hydraulic oil (Refilled) 	 120 Itr. (31.7 U.S. gal)

SPEC. NO. X21SP20010010

D375-llm

NO. X21SP20010010

D375-12m

KOMATSU D375A-5 GIANT R1PPKR

(Variable digging angle type)

Specifications

EQUIPMENT WEIGH:

(Additional weight to tractor) ..... 5470 kg (12,060 Ib)

DIMENSION:

Length

(Additional length to tractor).  2695 mm (8’10")

Ground pressure

(Additional pressure to tractor)  12 kPa (0.12 kgf/cm2/1.71 PSI)

RIPPER  EQUIPMENT:

Type	 Parallelogram, variable

digging angle type

Weight   	.... 5250 kg (11,570 Ib)

Beam length 	 1367 mm ( 4'6")

Shanks:

No. of shanks 	 1

Tooth point 	 Replaceable

Digging angle	 45 deg., STD, (available

stepless angle adjustment)

Digging depth	 Adjustable to 3 stages

Max. digging depth	 1435 mm ( 4’ 8")

Max. lift above ground 	 1060 mm { 3’ 6")

Hydraulic cylinders:

Type 	 Double-acting, piston type

No. of cylinders - bore:

Lifting cylinder	 2 - 225 mm (8.9")

Tilting cylinder	 2 - 200 mm (7.9")

HYDRAULIC EQUIPMENT:

Additional weight	 220 kg (  490 Ib)

Max. oil pressure 	 20.6 MPa (210 kgf/cm2/2,990PSI}

Hydrauliс pump:

Type	 Gear pump

Capacity (discharge flow) 	 405 Itr. (107 U.S. gal)/min

at engine rated rpm

Location 	 Rear of engine right side

Control valve 	 Spool type

Position:

Lifting spool 	 Raise, hold, lower and float

Tilting spool 	 Digging angle increase, hold

and decrease

Note: Lifting spool and tilting spool are change-overed with

selector valve.

Hydraulic tank:

type 	 Equipped with externally-

mounted control valve

Location		 Right of operator's seat

filter 	 Full-flow type

Hydraulic oil (Refilled) 	 70 Itr. (18.5 U.S. gal)

SPEC. NO. X21SP20010006

D375-37m

SPEC. NO. X21SP20010006

D375-38m

KOMATSU D375A-5 STEEL CAB

Specifications

EQUIPMENT WEIGH:

(Additional weight to tractor) ... 415 kg (910 Ib)

DIMENSION:

Overall height 	 4040 mm (13- 3")

Ground pressure

(Additional pressure to tractor). 1.0 kPa (0.01 kgf/cm2/0.14 PSI)

STEEL CAB:

Type 	All weather, enclosed type

Weight 	 415 kg	( 910 Ib)

Length 	1790 mm	( 5'10")

Width 	1455 mm	( 4' 9")

Height:

Cab height 	1675 mm	(	5' 6")

Floor mat to ceiling 	1530 mm	(	5' 0")

STANDARD EQUIPMENT:

Windshield wiper 	 4, front and rear windows,

left and right doors

Windshield washer 	 4, front and rear windows,

left and right doors

Room lamp 	 1

Cigarette light	 1

Ashtray 	 1

Floor mat	 1

OPTIONAL EQUIPMENT:

Air conditioner

Weight 	  60 kg (130 Ib)

Cooler 	 4500 kcal/hour

Heater 	 5000 kcal/hour

Additional heater 	 4000 kcal/hour

Room mirror 	 1

Sunvisor	 3, left, center and right

SPEC. NO. X21SP20010007

D375-39ra

SPEC. NO. X21SP20010007

D375-40m

KOMATSU D375-5 ROPS CANOPY

Specifications

EQUIPMENT WEIGH:

(Additional weight to tractor) .....760 kg (1,680 lb)

DIMENSION:

Overall  height   	4230 mm  (13'11")

Ground pressure

(Additional pressure to tractor) . 1.0 kPa (0.01 kgf/cra2/0.14 PSI)

ROPS CANOPY:

Type	  2-column ROPS canopy

Weight   	  760	kg	(1,680  lb)

Length 	  1405	mm	( 4’ 7")

Width 	  2035	mm	( 6’ 8")

Height (floor mat to roof) 	  1867	mm	( 6’ 2")

Roof area 	  2.30	m2	(3,565 in2)

Plate thickness 	  4.5	mm	(0.2")

Structure and strength comply with ISO 3417, SAE J1040 (April, 88), SAE J395 ROPS standards and ISO 3449 FOPS standards.

SPEC. NO. X21SP20010008

D375-41m

SPEC. NO. X21SP20010008

D375-42m

KOMATSU D375A-5 TRACTOR

ACCESSORY PARTS TABLE

Part No.     Part Name	Q'ty      Remarks

STARTING SWITCH KEY        2

PARTS BOOK                 1

OPERATION & MAINTENANCE    1

SPEC. NO. X21SP20010012

D375-7m

KOMATSU D375A-5 TRACTOR

OPTIONAL TOOL TABLE

Part No.     Part Name             Q’ty     Remarks

09000-30006   WRENCH SET           Is       8 x 10  12 x 14 13 x 17

19 x 22 24 X 27 30 X 32

09020-10284   SOCKET WRENCH SET    Is       10, 13, 14, 17, 19, 22,

24, 27, 30, 32, 36,

09033-00190   SCREWDRIVER	1

09036-00150   PLIERS	1

09339-00150   HAMMER	1

07952-80002   GREASE PUMP	1

07951-11400   NOZZLE	1

07950-90403   CARTRIDGE (GREASE)	1

09055-10390   BAR	1

09002-03641   WRENCH	1       36 x 41

09001-04600   WRENCH	1       46

09019-08035	WRENCH	1

09054-00009	THICKNESS GAUGE	1

09056-05513	TOOL BAG	1

SPEC. NO.X21SP20010012 D375-8m

KOMATSU D375A-5 TRACTOR

OPTIONAL SPARE PARTS TABLE

Part No.       Part Name        Q'ty     Remarks

07063-01142    ELEMENT           3       For transmission, steering

and hydraulic oil filter

07000-15175    0-RING            2       For transmission, and

steering oil filter

07000-15180	O-RING	1	For hydraulic oil filter

07000-13634	O-RING	6	For final drive drain plug

07020-00000	GREASE FITTING	4

6240-11-8810	GASKET	6	For cylinder head cover

6150-11-8820	RUBBER	36	For cylinder head cover

04122-22577	V-BELT	1	For cooling fan drive

6420-81-8720	V-BELT	1	For alternator drive

600-411-1171	CARTRIDGE	1	For corrosion resister

600-311-3110	CARTRIDGE	2	Fuel filter

600-211-1231	CARTRIDGE	2	For engine oil filter

0905Э-00800	SPARE PARTS BOX	1

SPEC. NO. X21SP20010012

D375-9m