BULLDOZERS COMPARISON TABLE

|  | Komatsu D355A-3 | CAT D9R | HSW TD40B | Liebherr PR751 |
| --- | --- | --- | --- | --- |
| Operating weight (kg) | 53,200 | 48,024 | 55,395 | 36,300 |
| Engine horsepower (HP) | 410 | 405 | 520 | 330 |
| Blade capacity (m3) | 11.40 | 16.40 | 19.00 | 9.15 |
| (------- | 628.83 | 683.25 | 817.98 | 478.57 |
| % | 100 | 109 | 130 | 76 |

PIPELAYERS COMPARISON TABLE

|  | Komatsu D355C-3 | CAT 589 | HSW SB85 | Liebherr RL461 |
| --- | --- | --- | --- | --- |
| Operating weight (kg) | 57,600 | 65,366 |
| Engine horsepower (HP) | 360 | 420 |
| Lifting capacity (kg) | 92,000 | 104,000 |
| (------- | 124.02 | 141.86 |
| % | 100 | 114 |

HYDRAULIC EXCAVATORS

COMPARISON TABLE

|  | Komatsu PC400-6 | CAT 350L | Hitachi EX400-3 | Kato HD1880SE | Kato HD1800SV-S |
| --- | --- | --- | --- | --- | --- |
| Operating weight (kg) | 41,400 | 50,020 | 41,000 |
| Engine horsepower (HP) | 306 | 286 | 296 |
| Bucket capacity (m3) | 1.80 | 3.1 | 1.82 |
| (------- | 283.57 | 353.96 | 280.57 |
| % | 100 | 125 | 99 |

| COMPARISON TABLE |
| --- |
| SPEC | D355A-3 | D9L | D9R |
| ENGINE HORSEPOWER (HP) | 410 | 460 | 405 |
| OPERATING WEIGHT (t) | 53.2 | 58.03 | 48.02 |
| (------- | 148 | 164 | 139 |
| % | 100 | 111 | 94 |
| TRACK GAUGE (mm) | 2260 | 2500 | 2250 |
| TRACK LENGTH ON GROUND (mm) | 3360 | 3546 | 3474 |
| LINK PITCH (mm) | 260.5 | 228.6 | 240 |
| IDLER DIA (mm) | 880 | 740 | 720 |
| BUSH DIA (mm) | 87.9 | 82 | 85 |
| PIN DIA (mm) | 55.6 | 50.8 | 50.9 |
|  | TRAVEL SPEED (km/h) |
|  | Forward 1-st | 3.3 | 3.9 | 3.9 |
| 2-nd | 5.1 | 7.2 | 6.8 |
| 3-rd | 8.5 | 12.4 | 11.8 |
| 4-th | 12.7 |
| Reverse 1-st | 3.2 | 5.1 | 4.8 |
| 2-nd | 5.0 | 9.0 | 8.4 |
| 3-rd | 8.4 | 15.4 | 14.7 |
| 4-th | 12.6 |
|  | BULLDOZER EQUIPMENT |
|  | Blade: Length (mm) | 4,315 | 4,541 | 4,314 |
| Height (mm) | 1,875 | 1,988 | 1,934 |
|  | DIMENSIONS: |
|  | Overall length (mm) | 9,630 | - | 7,182 |
| Overall width (mm) | 3,030 | 3,186 | 2,860 |
| Overall height (mm) | 4,125 | 3,163 | 3,912 |
| Ground clearance (mm) | 575 | - | 507 |
| Track gauge (mm) | 2,260 | 2,500 | 2,250 |
| Length of track on the ground (mm) | 3,360 | 3,546 | 3,474 |

| ENGINE |
| --- |
|  | Model | Komatsu SA6D155 | Caterpillar 3412 | Caterpillar 3408C |
| Type | Direct injection Turbocharged | Turbocharged | Direct injection Turbocharged |

No of cylinders -

| bore x stroke (mm) | 6-155 x 170 | 12-137 x 152 | 8-137 x 152 |
| --- | --- | --- | --- |
| Piston displacement (l) | 19.26 | 27.00 | 18.00 |
| POWER TRAIN |
|  | Torque converter, Damper or Main Clutch |

Single stage T/C

|  | Single stage T/C | Single stage T/C |
| --- | --- | --- |
| Transmission |

Planetary gear

Multiple disc

Planetary gear

Planetary gear

| Multiple disc |
| --- |
| Steering clutch | Wet | - | Wet multiple disc |
| Brake | Wet multiple disc | - | Wet multiple disc |
| Final drive |

Planetary and spur gear

| Double reduction | - |
| --- | --- |

Planetary gear

Double reduction

| COMPARISON TABLE |
| --- |
| SPEC | PC400-6 | HD1880 |
| ENGINE HORSEPOWER (HP) | 306 | 253 |
| OPERATING WEIGHT (kg) | 41,400 | 41,000 |
| BUCKET CAPACITY (m3) | 1.8 | 1.8 |
| ARM CROWD FORCE (Ton) (short arm) | 26.2 | 19.9 |
| SWING SPEED (RPM) | 9.3 | 7.8 |
| TRAVEL SPEED (km/h) |
| High | 5.5 | 4.3 |
| Low | 3.2 | 2.9 |
| MAX. DIGGING DEPTH (mm) | 7,760 | 7,280 |
| TRACK LENGTH (mm) | 5,025 | 4,730 |