DIFFERENCE BETWEEN PC400-5 AND PC400-6

PC400-5

|  | PC400-6 |
| --- | --- |

| HYDRAULIC SYSTEM |
| --- |
| OLSS | HydrauMind |

HIGH OUTPUT ENGINE

Engine model S6D125

Rated output 206(276)/2000

Engine model SA6D125E

Rated output 228(306)/1950

| LARGE DIGGING FORCE |
| --- |
| 21.0t | 22.9t |

| ARM REGENERATION CIRCUIT |
| --- |
| Not available | Available |

| HIGH DURABILITY AND RELIABILITY |
| --- |
|  | Increasing of sectional dimensions of boom |
|  | Increasing of sectional dimensions of arm |

| TRACK LINKS |
| --- |
| Track link type |
| Without strut | With strut |
| Link pitch |
| 216 | 228.6 |

| OPERATOR’S INVIRONMENT |
| --- |
| Cab size |
| 940 x 1594 | 990 x 1800 |
| Seat sliding method |
| Seat only slide | Seat and control lever slide together |
| Control lever type |
| Long lever | Wrist control lever |
| Seat back pocket |
| Not provided | Provided |

| SERVICE AND SAFETY |
| --- |
| Type of pump/engine partition |
| Muffler cover only | Full partition |
| Turbocharger exhaust manifold cover |
| Not provided | Provided |
| Large handrail |

Height from deck 930

Height from hood 200

Height from deck 1260

Height from hood 500

РАЗЛИЧИЯ МЕЖДУ PC400-5 И PC400-6

PC400-5

|  | PC400-6 |
| --- | --- |
| ГИДРАВЛИЧЕСКАЯ СИСТЕМА |
| OLSS (Система контроля нагрузки с открытым центром) | HydrauMind (Гидравлическая система саморегуляции) |

БОЛЕЕ МОЩНЫЙ ДВИГАТЕЛЬ

Модель двигателя     S6D125

Мощность 206(276)/2000

Модель двигателя SA6D125E

Мощность 228(306)/1950

| УВЕЛИЧЕНО УСИЛИЕ КОПАНИЯ |
| --- |
| 21.0т | 22.9т |

| ЦЕПЬ ВОССТАНОВЛЕНИЯ ДАВЛЕНИЯ ЦИЛИНДРА РУКОЯТИ |
| --- |
| Отсутствует | Установлена |

| ВЫСОКАЯ НАДЕЖНОСТЬ |
| --- |
|  | Увеличены размеры сечения стрелы |
|  | Увеличены размеры сечения рукояти |

| ГУСЕНИЦЫ |
| --- |
| Тип гусениц |
| Без перемычки | С перемычкой |
| Шаг звена |
| 216 | 228.6 |

| УСЛОВИЯ РАБОТЫ ОПЕРАТОРА |
| --- |
| Размер кабины |
| 940 x 1594 | 990 x 1800 |
| Способ перемещения сидения |
| Перемещается только сидение | Перемещение сидения с рычагами |
| Тип рычага управления |
| Длинный рычаг | Короткий рычаг типа “Джойстик” |
| Карман на спинке сидения |
| Отсутствует | Установлен |

| ОБСЛУЖИВАНИЕ И БЕЗОПАСНОСТЬ |
| --- |
| Тип перегородки двигатель/насос |
| Только между глушителем | Полное разделение |
| Крышка на выхлопном турбонагнетателе |
| Отсутствует | Установлена |
| Поручни |

Высота от капота 930

Высота от подножки 200

Высота от капота 1260

Высота от подножки 500