# KOMATSU PC400-6 EXCEL HYDRAULIC EXCAVATOR

Arm 3380 mm

Boom 7060 mm

Bucket: SAE heaped 1.80 m3 (2.35 cu.yd) Backhoe

Shoe: 600 mm(24”) Triple

Air conditioner

Sandy area arrangement

For –20C - + 40C operation

KOMATSU PC400-6 EXCEL HYDRAULIC EXCAVATOR

(BACKHOE)

Specifications
OPERATING WEIGHT 	 41400 kg ( 91,270 Ib)

Including lubricant, full fuel tank, hydraulic oil, operator and Boom :   7060 mm (23' 2") One-piece

Arm  :   3380 mm (11' 1")

Bucket : SAE heaped  1.80 m3 ( 2.35 cu.yd) Backhoe

Shoe :   600 mm (24") Triple

FLYWHEEL HORSEPOWER

SAE J1349 	228 kW (306 HP) /1950 RPM

DIN 6270 	228 kW (310 PS) /1950 RPM

BUCKET CAPACITY

SAE heaped 	1.80 m3 ( 2.35 cu. yd)

CECE heaped 	1.60 m3 ( 2.09 cu.yd)

BUCKET WIDTH

Without side cutters 	1425 mm (56.1")

With side cutters 	1575 mm (62.0")

BOOM LENGTH 	7060 mm (23'2")

ARM LENGTH 	3380 mm (11'1")

DIGGING FORCE

Bucket digging force 	  225 kN (22900 kg/50,490 Ib)

Arm crowd force 	  192 kN (19600 kg/43,210 Ib)

ENGINE

Manufacturer 	Komatsu

Model 	SA6D125E-2

Cooling system 	Water cooled

Aspiration 	Turbocharged and aftercooled

No. of cylinders 	6

Bore 	125 mm ( 4.92")

Stroke 	150 mm ( 5.91")

Piston displacement 	11.04 Itr. ( 674 cu.in)

Performance:

Max. torque 	1213 N.m (123.7 kg.m/895 Ib.ft)

Engine RPM at max. torque 	1400 rpm

Fuel system:

Fuel 	Diesel gas oil, ASTM

Specification D975-60T No. 2D

Combustion method 	Direct injection

Governor type 	Mechanical, all-speed control

Lubrication system:

Lubrication method 	Forced lubrication

Lubrication pump 	Gear pump

Lubrication filter 	Full-flow

SPEC. NO. X21SP970008

PC400 EXCEL-Ih

Cooling method 	 Water cooled

Cooling method 	Forced circulation by

centrifugal water pump

Fan type 	Suction type

Air cleaner type 	Dry type with automatic

dust evacuator Starting system:

Starting method 	By electric motor

Starting motor voltage 	24 V

Starting capacity 	7.5 kW

Alternator voltage 	24 V

Alternator amperage 	33 A

Battery 	2 x  12 V/  150 Ah

HYDRAULIC SYSTEM:

Type 	HydrauMind system

Main pump

Type 	Variable capacity piston pump

No. оf pump 	2

Maximum flow 	616 Itr. /min.

(162.7 U.S.gal/ min.) Relief valve settings

Implement circuits 	34.8 MPa (355 kg/cm2/5, 050 PSI)

Travel circuits 	34.8 MPa (355 kg/cm2/5, 050 PSI)

Swing circuits 	27.9 MPa (285 kg/cm2/4, 050 PSI)

Pilot circuits 	 2.9 MPa ( 30 kg/cm2/  430 PSI)

Control valve

Type 	6 + 1 spool type x 1

Hydraulic motor

Travel 	Axial piston type  x 2

Swing 	Axial piston type  x 1

No. of cylinders-bore x stroke x rod dia.

Boom 	2-160 mm x 1570 mm x 110 mm

( 6.3" x  61.8" x  4.3")

Arm 	1-185 mm x 1820 mm x 120 mm

( 7.3" x  71.7" x  4.7")

Bucket 	1-160 mm x 1270 mm x 110 mm

( 6.3" x  50.0" x  4.3")

OPERATOR'S CAB:

Type 	All weather, enclosed type

IMPLEMENT CONTROLS:

Type 	Two levers actuated boom, arm

bucket and swing

STEERING CONTROLS:

Type 	Two-lever

DRIVE:

Drive method 	 Hydrostatic

Reduction system 	 Planetary gear,

double-reduction
Max. drawbar pull 	330 kN (33700 kg/74, 300 Ib)

SPEC. NO. X21SP970008

PC400 EXCEL-2h

Max. travel speed (High) 	5.5 km/h ( 3.4 MPH)

Max. travel speed (Low) 	3.2 km/h (2.0 MPH)

Gradeability 	70 % ( 35 deg )

BRAKE: Travel

Service brake 	 Hydraulic lock

Parking brake 	 Wet, multiple-disc brake

Swing

Service brake 	 Hydraulic lock

Holding brake 	 Wet, multiple-disc brake

UNDERCARRIAGE:

Type 	 Crawler-tractor-design

undercarriage

Center frame 	 X-leg frame

Track frame 	 Box-section

Seal of track 	 Sealed track

Track adjuster 	 Hydraulic type

Rollers type 	 Floating seal

Track shoes

Type 	 Triple

No. of shoes 	 46 each side

No. of rollers

Carrier rollers 	 2  each side

Track rollers 	 7  each side

Ground pressure 	 77.5 kPa (0.79 kg/cm2 /11.23 PSi;

SWING SYSTEM:

Drive method 	 Hydrostatic

Reduction system 	 Planetary gear,

double-reduction
Swing circle bearing 	 Single row shear type

ball bearing
Swing speed 	 9.3 RPM

SERVICE REFILL CAPACITIES:

Fuel tank 		605.0 Itr.	(	159.8 U.S.gal)

Radiator 		47.0 Itr.	(	12 .4 U.S. gal)

Engine 		32.0 Itr.	(	8.5 U.S. gal)

Final drive, each side 		11.5 Itr.	(	3.0 U.S. gal)

Swing drive 		21.5 Itr.	(	5.7 U.S. gal)

Hydraulic system 		270.0 Itr.	(	71.3 U.S.gal)

SPEC. NO. X21SP970008

PC400 EXCEL-3h

KOMATSU PC400-6 EXCEL HYDRAULIC EXCAVATOR

(BACKHOE)

DIMENSIONS

7060 mm (23' 2") BOOM

3380 mm (11' 1") ARM

A: Overall length 	11835 mm	(38'10")

B: Overall width 	3430 mm	(11'3")

C: Overall height (to top of boom) 	3635 mm	(11'11")

D: Overall height (to top of cab) 	3265 mm	(10'9")

E: Ground clearance, counterweight	1320 mm	( 4'4")

F: Min. ground clearance 	555 mm	 ( 1'10")

G: Tail swing radius 	3500 mm	(II16")

H: Length of track on ground	4020 mm	(13'2")

I: Track length	5025 mm	(16'6")

J: Track gauge	2740 mm	( 9'0")

K: Width of crawler 	3340 mm	(10'11")

L: Shoe width 	600 mm	 (   24")

M: Grouser height 	37 mm	  (  1.5")

N: Machine cab height 	2365 mm	 (7'9")

O: Machine cab width 	2995 mm	 (9'10")

P: Distance, swing center to rear end 	3500 mm	 (11'6")

Q: Length on ground (transport) 	6520 mm	 (21'5")

KOMATSU PC400-6 EXCEL HYDRAULIC EXCAVATOR

(BACKHOE)

WORKING RANGE

7060 mm (23' 2 " ) BOOM

3380 mm (11' 1") ARM

A:  Max. digging height 	10920 mm	(35'	4")

A* : Max. digging height 	11445 mm	(37 '	7 ")

B:  Max. dumping height 	 7570 mm (24'10")

B* : Max. dumping height 	 7395 mm.(22'	3")

C:  Max. digging depth 	 7760 mm	(25'	6")

C*: Max. digging depth 	 7945 mm	(26 '	1")

D:  Max. vertical wall digging depth 	 6850 mm	(22'	6")

E:  Max. digging depth of cut for 8' level 	 7620 mm	(25'	0")

F:  Max. digging reach 	12020 mm	(39'	5")

F*: Max. digging reach 	12195 mm	(40'	0")

G:  Max. digging reach at ground level 	11810 mm	(38'	9")

G* : Max. digging reach at ground level 	11995 mm	(39'	4")

H:  Min. swing radius 	 4770 mm	(15'	8")

I:  Max. height of min. swing radius 	 9200 mm	(30 '	2" )

Note: * indicates working range when front shovel.

KOMATSU PC400-6 EXCEL HYDRAULIC	EXCAVATOR

(BACKHOE)

ACCESSORY PARTS TABLE

Part No.    Part Name	 Q'tv      Remarks

STARTING SWITCH KEY		2

PARTS BOOK	1

OPERATION & MAINTENANCE MANUAL       1

SPEC.NO. X21SP970008 PC400 EXCEL-7h

KOMATSU PC400-6 EXCEL HYDRAULIC EXCAVATOR

(BACKHOE)

OPTIONAL TOOL TABLE

Part No.        Part Name	 Q'tv          Remarks
09056-05513     TOOL BAG	  1

09019-08035     WRENCH	1	For filter

207-98-61130    SOCKET WRENCH	1

09033-00190     SCREWDRIVER	1

09039-00150     HAMMER	1

09055-10390     BAR	1

07950-10450     GREASE PUMP	1

07951-31400     NOZZLE	1

07950-90403     CARTRIDGE(GREASE)	1

09002-03641     WRENCH	1

09002-01317     WRENCH	1

09002-01922     WRENCH	1

09007-00836     WRENCH	1

SPEC. NO. X21SP970008 PC400 EXCEL-8h

KOMATSU PC400-6	EXCEL HYDRAULIC EXCAVATOR

(BACKHOE)

OPTIONAL	SPARE PARTS TABLE

Part No.	Part Name              Q'tv		Remarks

6150-11-7812	GASKET	6		For engine rocker cover

6150-11-8810	GASKET	6		For engine heal cover

6150-11-8820	RUBBER	24		For engine head cover

600-211-1230	CARTRIDGE	1		For engine oil filter

600-311-8292	CARTRIDGE	1		For fuel filter

04121-22262	BELT	1		For cooling fan

07002-22434	0-RING	1		For engine oil drain plug

208-60-61180	ELEMENT	1		For hydraulic filter

07000-05210	0-RING	1		For hydraulic filter

07002-01223	0-RING	1		For P.Т.О. drain plug

07002-02434	0-RING	4

07020-00000	FITTING	4

07020-00675	FITTING	4

07020-00900	FITTING	1

20Y-60-21470	ELEMENT	1		For hydraulic tank

20Y-60-21470	208-98-61110	SPARE PARTS TABLE	1

SPEC. NO. X21SP970008 PC400 EXCEL-9h

KOMATSU PC400-6 EXCEL HYDRAULIC EXCAVATOR

(BACKHOE)

LIFTING CAPACITY

.7060 mm (23'2") Boom

.1.80m3 (2.35 cu.yd) SAE heaped bucket

.600 mm (24") width triple grouser shoe

unit: kg Ib

*: Load is limited by hydraulic capacity rather than tipping. Ratings are based on SAE Standard No. J1097. Rated loads do notexceed 87 % of hydraulic capacity or 75 % of tipping load.

Specifications are subject to change without notice.

SPEC. NO. X21SP970008 PC400 EXCEL-lOh