“Gayskiy GOK”

KOMATSU  PC750SE-7

HYDRAULIC EXCAVATOR

4,0 m3 (SAE) BUCKET,

BOOM  LENGTH 7100 mm.

ARM LENGTH 2945 mm,

STEEL CAB,

AIR CONDITIONER,

610mm SHOES.

FOR

ATMOSPHEROC TEMPERATURE FROM -30 C UP TO +40 C

KOMATSU PC700SE-7 HYDRAULIC EXCAVATOR

Specifications

| OPERATING WEIGHT | 73 170 kg |
| --- | --- |
| Including lubricant, full fuel tank, hydraulic oil, operator and Boom: 7 100 mm Arm: 2 945 mm Bucket: 4.0 m3 (SAE), Backhoe Shoe: 610 mm, Double grouser. |
| FLYWHEEL HORSEPOWER: |  |
| SAE (J1349) | 338 kW(454 H.P.) / 1800 RPM |
| DIN (6270) | 338 kW (460 PS) / 1800 RPM |
| BUCKET CAPACITY |  |
| SAE | 4.0 m3 |
| СЕСЕ | 3.5 m3 |
| BUCKET WDTH: |  |
| Without side cutters | 2 000 mm |
| With side cutters | 2 100 mm |
| BOOM LENGTH | 7 100 mm |
| ARM LENGTH | 2 945 mm |
| DIGGING FORCE (at power max.) |  |
| Bucket diggiing force (SAE) | 391 кН (39 900 kg) |
| Bucket digging force (ISO) | 431 кН (43 900 kg) |
| Arm crowd force (SAE) | 331 кН (33 800 kg) |
| Arm crowd force (ISO) | 341 кН (34 800 kg) |
| ENGINE: |  |
| MANUFACTURED | KOMATSU |
| MODEL | SAА6D140Е-3 |
| COOLANT SYSTEM | WATER COOLED |
| ASPIRATION | TURBOCHARGED AND AFTERCOOLED |
| No. OF CYLINDERS | 6 |
| BORE | 140 mm |
| STROKE | 165 mm |
| PISTON DISPLACEMENT | 15.24 ltr |
| PERFORMANCE: |  |
| Max. torque | 2 108 N.m (215kg.m) |
| Engine RPM at max. torque | 1 350 rpm |
| FUEL SYSTEM: |  |
| FUEL | DIESEL GAS OIL, ASTM SPECIFICATION D975-60T No. 2D |
| COMBUSTION METHOD | DIRECT INJECTION |
| GOVERNOR | ELECTRONIC, ALL SPEED CONTROL |
| LUBRICATION SYSTEM: |  |
| LUBRICATION METHOD | FORCED LUBRICATION |
| LUBRICATION PUMP | GEAR PUMP |
| LUBRICATION FILTER | FULL-FLOW |
| COOLING METHOD | WATER COOLED |
| COOLING METHOD | FORCED CIRCULATION BY CENTRIFUGAL WATER PUMP |
| FUN TYPE | SUCTION TYPE |
| AIR CLEANER TYPE: | DRY TYPE WITH AUTOMATIC DUST EVACUATOR |
| STARTING SYSTEM: |  |
| STARTING METHOD | BY ELECTRIC MOTOR |
| STARTING MOTOR | 24 V |
| STARTING MOTOR POWER | 11 Kw |
| ALTERNATOR VOLTAGE 24V |
| ALTERNATOR AMPERAGE 75A |
| BATTERY | 12 V Х 2 – 200 А/h |
| HYDRAULIC SYSTEM: |  |
| TYPE | OLSS (OPEN-CENTER LOAD SENSING SYSTEM) |
| No. OF SELECTABLE MODE | 2 |
| MAIN PUMP: |  |
| TYPE | VARIABLE DISPLACEMENT PISTON |
| No. OF PUMP | 2 |
| MAXIMUMS FLOW ( TOTAL) | 988 ltr/min (261 U.S. gal/min) |
| SUB PUMP |  |
| TYPE | GEAR PUMP |
| RELIEF VALVA SETTINGS: |  |
| SWING | 290 kg/сm2 |
| IMPLEMENT CIRCUITS | 320 kg/сm2 |
| TRAVEL CIRCUITS | 350 kg/сm2 |
| WHEN HEAVY LIFT | 350 kg/сm2 |
| PILOT CIRCUITS | 30 kg/сm2 |
| CONTROL VALVE: |  |
| TYPE | 4- SPOOL TYPE X 1 5-SPOOL TYPE X 1 |
| HYDRAULIC MOTOR: |  |
| TRAVEL | PISTON TYPE X 2 |
| SWING | PISTON TYPE X 2 |
| No. OF CYLINDERS, BORE X STROKE X ROD DIA: |  |
| BOOM | 2-200 mm Х 1950 mm Х 140 mm |
| ARM | 2-185 mm Х 1610 mm Х 120 mm |
| BUCKET | 1-225 mm Х 1420 mm Х 160 mm |
| OPERATORS'S CAB: |  |
| TYPE | ALL WEATHER, ENCLOSED TYPE |
| IMPLEMENT CONTROLS: |  |
| TYPE | TWO LEVERS ACTUATED BOOM, ARM, BUCKET AND SWING |
| STEERING CONTROL: |  |
| TYPE | TWO-LEVER WITH PEDAL |
| DRIVE: |  |
| DRIVE METHOD | HYDROSTATIC |
| REDUCTION SYSTEM | 3-STAGE PLANETARY GEAR |
| MAXIMIM DRAWBAR PULL | 559 kN (57 000 kgf) |
| MAXIMIN TRAVEL SPWWD ( HIGH) | 4.2 km/h |
| MAXIMIN TRAVEL SPEED (LOW) | 2.8 km/h |
| GREADEBILITY | 70% (35º) |
| BRAKE: |  |
| TRAVEL: |  |
| SERVICE BRAKE | HYDRAULIC LOCK |
| PARKING BRAKE | WET, MULTIPLE-DISC BRAKE |
| SWING: |  |
| SERVICE BRAKE | HYDRAULIC LOCK |
| HOLDING BRAKE | WET, MULTIPLE-DISC BRAKE |
| UNDERCARRIAGE: |  |
| TYPE | CRAWLER-TRACTOR-DESIGN UNDERCARRIAGE |
| CENTRAL FRAME | H-LEG FRAME |
| TRACK FRAME | BOX-SECTION |
| SEAL OF TRACK | SEALED TRACK |
| TRACK ADJUSTER | HYDRAULIC TYPE |
| ROLLER TYPE | FLOATING SEAL |
| TRACK SHOES: |  |
| TYPE | DOUBLE GROUSER |
| No. OF SHOES | 47 EACH SIDE |
| No. OF ROLLERS: |  |
| CARRIER ROLLERS | 3 EACH SIDE |
| TRACK ROLLERS | 8 EACH SIDE |
| GROUND PRESSURE | 1.22 kg/сm2 |
| SWING SYSTEM |  |
| DRIVE METHOD | HYDROSTATIC |
| REDUCTION SYSTEM | PLANETARY GEAR |
| SWING CIRCLE BEARING | SINGLE ROW SHEAR TYPE BALL BEARING |
| SWING SPEED | 6.8 RPM |
| SERVICE REFILL CAPACITIES: |  |
| FUEL TANK | 880 ltr |
| REDIATOR | 85 ltr |
| ENGINE | 55 ltr |
| FINAL DRIVE, EACH SIDE | 20 ltr |
| SWING DRIVE | 24.5 ltr |
| HYDRAULIC SYSTEM | 440 ltr |

KOMATSU  PС750SE-7 HYDRAIULIC EXCAVATOR

WORKING RANGE

BOOM 7 100 mm

ARM    2 945 mm

| А: MAX. DIGGING HEIGHT | 11 330 mm |
| --- | --- |
| В: MAX DUMPING HEIGHT | 7 525 mm |
| С: MAX. DIGGING DEPTH | 7 130 mm |
| D: МАX. VERTICAL WALL DIGGING DEPTH | 4 080 mm |
| Е: MAX. DIGGING DEPTH OF CUT FOR 8' LEVEL | 6 980 mm |
| F: MAX. DIGGING REACH | 12 265 mm |
| G: MAX. DIGGING REACH ON GROUND LEVEL | 11 945 mm |
| Н: MIN. SWING RADIUS | 5 645 mm |
| I: MAX.HEIGHT OF MIN. SWING | 9 570 mm |

KOMATSU  PС750SE-7 HYDRAILIC EXCAVATOR

DIMANSIONS

| BOOM 7 100 mm ARM 2 945 mm |
| --- |
| А: OVERALL LENGTH | 13 030 mm |
| B: OVERALL WIDTH | 4 110 mm |
| С: OVERALL HEIGHT (TO TOP OF BOOM) | 4 615 mm |
| D: OVERALL HEIGHT (TO TOP OF CAB) | 3 560 mm |
| E: GRAUND CLEARANCE COUNTERWEIGHT | 1 560 mm |
| F: GROUND CLEARANCE (MINIMUM) | 840 mm |
| G:TALL SWING RADIUS | 4 245 mm |
| Н: TRACK LENGTH ON GROUND | 4 500 mm |
| I: TRACK LENGTH | 5 810 mm |
| J: TRACK GAUGE | 3 500 mm |
| К: WIDTH OF CRAWLER | 4 110 mm |
| WITH OF CRAWLER (WHEN RETRACTED) | 3 390 mm |
| L: SHOE WIDTH | 610 mm |
| М: GROUSER HEIGHT | 50 mm |
| N: MACHINE CAB HEIGHT | 3 445 mm |
| 0: MACHINE CAB WIDTH | 4 000 mm |
| P: DISTANCE, SWING CENTER TO REAR END | 4 245 mm |

KOMATSU  PС750SE-7 HYDRAIULIC EXCAVATOR

ACCESSORY PARTS TABLE

| PART No. | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
|  | STARTING SWITCH KEY | 2 |  |
|  | OPERATION & MAINTANANCE MANUAL | 1 |  |
|  | PARTS BOOK | 1 |  |

KOMATSU  PС750SE-7 HYDRAIULIC EXCAVATOR

OPTIONAL TOOL TABLE

| PART No. | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
| 07950-90403 | CARTRIDGE | 1 |  |
| 07952-70004 | GREASE PUMP | 1 |  |
| 09002-01922 | WRENCH | 1 |  |
| 09002-00836 | WRENCH | 1 |  |
| 09007-01040 | WRENCH | 1 |  |
| 21T-98-64120 | WRENCH | 1 |  |
| 209-98-77310 | TOOL KIT | 1 |  |
| 09033-00190 | DRIVER | 1 |  |
| 09039-00150 | HAMMER | 1 |  |
| 09055-10390 | BAR PINCH | 1 |  |
| 09056-04613 | TOOL BAG | 1 |  |
| 07286-01690 | HOSE | 2 |  |

KOMATSU  PС750SE-7 HYDRAIULIC EXCAVATOR

OPTIONAL SPARE PARTS TABLE

| PART No. | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
| 600-211-1340 | CARTRIDGE | 1 |  |
| 600-319-3310 | CARTRIDGE | 1 |  |
| 600-411-1171 | CARTRIDGE | 1 |  |
| 600-185-6100 | ELEMENT ASS | 1 |  |
| 600-736-9730 | V-BELT | 1 |  |
| 6210-81-6960 | V-BELT | 1 |  |
| 209-60-77530 | ELEMENT | 2 |  |
| 07000-15180 | O-RING | 2 | FOR HYDRAULIC OIL RETURN FILTER |
| 209-60-76210 | FILTER CARTRIDGE | 1 |  |
| 07002-13034 | O-RING | 4 |  |
| 07002-22343 | O-RING | 1 |  |
| 424-16-11140 | OIL FILTER ELEM ASS | 1 |  |
| 424-16-11130 | O-RING | 1 |  |
| 419-15-14870 | GASKET | 1 |  |
| 419-15-14860 | O-RING | 1 |  |
| 07002-11223 | O-RING | 1 |  |
| 209-98-77250 | TABLE SPARE PARTS | 1 |  |
| 209-98-77260 | ACCESORY TABLE | 1 |  |

KOMATSU  PС750SE-7 HYDRAIULIC EXCAVATOR

OPTIONAL LIST

DESCRIPTION

BATTERIES – LARGE

ALTERNATOR – 75 A

BOOM -7 100 mm

ARM-  2 945 mm

BUCKET 4 cub.m. WITH   TEETH  ROCK PENETRATOR (RP3)

COLD ARRANGE (-30C)

COOLANT HEATER ELECTRIC TYPE (230V, 1 500W)

ENGINE  OIL PAN HEATER ELECTRIC TYPE (230V, 600W)

COMBUSTION TYPE COOLANT HEATER

(INSTALL TYPE, HOT WATER 3 500 KCAL/H, HOT AIR 4 000 KCAL/H)

SANDY AREA ARRANGE

POOR FUEL, WATER+DUST

FLUSH LIGHT

TRAVEL ALARM

INTERCONNECTED HORN

REAR VIEW MIRROR, LH

LIGHT, AMBER BEACON

FOPS

CAB FRONT FULL GUARD

SEAT BELT 78 mm

AUTO AIR CONDITIONER LARGE CAPACITY :

COOLING 4 300 KCAL/H & HETER 5 000 KCAL/H.

RADIO AM/FM

12V E/SUPPLY

SUN VISOR

WINDOW WIPER, FRONT

CATWALK

COUNTERWEIGHT

TRACK FRAME UNDERCOVER

DOUBLE FLANGE  T. ROLLER

FIRE EXTINGIUSER

CAP & OVERAL

GENERAL TOOL KIT

SPARE PARTS -GENERAL

RUSSIAN PLATE

# Text boxes

ДИАМ.

ХОД

КОЛ-ВО ЦИЛИНДРОВ

РАБОЧИЙ ОБЪЕМ

РАБОЧИЕ ХАРАКТЕРИСТИКИ ДВИГАТЕЛЯ