# KOMATSU BULLDOZER

## D355A-3

### WITH

STRAIGHT TILT DOZER

GIANT RIPPER

#### ROPS TYPE STEEL CAB

FOR –50oC~ +40oC OPERATION

(WITH STARTING ENGINE)

GENERAL SPECIFICATIONS

OPERATING WEIGHT.............................………………………   53,590 kg

DIMENSIONS:

Overall length...........................…………………………..   9630 mm

Overall width............................…………………………...  4315 mm

Overall height..............................…………………………  4125 mm

# Ground pressure........................………………………….   1.31 kg/cm2

CONTENTS

1. D355A-3 TRACTOR SPECIFICATIONS

2. EXCLUSIVE ENGINE PREHEATER SPECIFICATIONS

3. STRAIGHT-TILTDOZER SPECIFICATIONS

4. GIANT RIPPER SPECIFICATIONS

5. ROPS TYPE STEEL CAB SPECIFICATIONS

6. STANDARD TOOL, SPARE PARTS AND ACCESSORY TABLES

## KOMATSU  D355A-3  TRACTOR

## Specification

OPERATING WIGHT ................................………………………  36,930 kg

FLYWHEEL HORSEPOWER ............................………………… 410 HP

PERFORMANCE:

Travel speed and rated drawbar pull:   (Refer to the attached sheet)

Travel speed

Forward        1st...........................………………………… 0 -  3.3 km/h

2nd...........................……………………….  0 -  5.1 km/h

3rd...........................………………………..  0 -  8.5 km/h

4th...........................………………………..  0 - 12.7 km/h

# Reverse         1st...........................………………………… 0 -   3.2 km/h

2nd...........................……………………….   0 -  5.0 km/h

3rd...........................………………………..  0 -   8.4 km/h

4th...........................………………………..  0 - 12.6 km/h

Turning radius...............................…………………………………  3.7 m

DIMENSIONS:

Overall length...........................……………………………  5,405 mm

Overall width............................……………………………  3,030 mm

Overall height:

To top of exhaust pipe..................…………………………  4,125 mm

To highest point, exclusive of exhaust pipe.........................  2,890 mm

(to top of precleaner cover)

Track gauge.............................…………………………….   2,260 mm

Length of track on ground...............……………………….   3,360 mm

Ground contact area.....................………………………….  40,990 cm2

Ground pressure.........................…………………………… 0.90 kg/cm2

Ground clearance........................…………………………..   575 mm

ENGINE:

Model...................................……………………………  KOMATSU SA6D155-4A

Type....................................…………………………….  Water cooled,  4-cycle

overhead valve,

direct injection type,

turbocharged diesel engine

with after cooler

No. of cylinders - bore x stroke........…………………… 6-155 mm x 170 mm

Piston displacement.....................………………………  19,260 cc

Performance,

Rated RPM...............................…………………………  2000 RPM

Flywheel horsepower.....................……………………..  410 HP

Max. torque..............................…………………………  176 kg.m/1400 RPM

Fuel system:

# Fuel oil................................…………………………….  According to  KOMATSU

# recommendation

Governor................................…………………………..   Mechanical,

all speed control

Lubrication system:

Lubricating method......................………………………  Gear pump,

forced lubrication

Filter..................................……………………………..    Full-flow and

by-pass type

Oil cooler..............................……………………………  Water-cooled

Cooling system...............................……………………………..   Forced circulation, by

centrifugal water pump,

reversible fan

Air cleaner..................................……………………………….    Dry type with automatic

dust ejector and dust

indicator

Starting method..............................……………………………..   By electric starting motor

Starting motor..........................………………………….   24 V, 11 kW

Starting aid

Coolant heater (electric type)..........…………………….   230 V, 4 kW x 1,

1.5 kW x 1

Oil pan heater (electric type)..........……………………..   230 V, 600 W x 2

Battery warmer..........................…………………………  Engine coolant type,

felt type case

Engine side cover.......................………………………..   Closed type

Rocket heater (attached type)...........……………………   30,000 kcal/H

# Ether spray system

Air intake system from

bonnet side port

Radiator shutter........................………………………….  Metal type

Engine room kilting.....................……………………….. Cloth type

Alternator...................................………………………………… 24 V, 50 A

Battery......................................………………………………….  12 V x 200 Ah x 2

POWER TRANSMITTING SYSTEM:

Torque converter:

Type....................................……………………………… 3 element, single stage

and single phase

Cooling method.........................………………………….  Water-cooled

Transmission:

Type....................................………………………………. Planetary gear and

multiple disc clutch,

hydraulically actuated,

forced lubrication

Gear shift.............................……………………………… 4 forward and

4 reverse  speeds

Bevel gear...................................…………………………………  Spiral bevel gear

Steering system:

Steering clutch.........................…………………………… Wet, multiple disc,

spring loaded,

hand operated,

hydraulically actuated

Steering brake..........................…………………………… Wet, contacting band,

foot operated,

interconnected  with

steering clutch, with

hydraulic booster

Final drive..................................…………………………………. Spur gear single

reduction and

planetary gear single

reduction

UNDERCARRIAGE:

Suspension ..................................………………………………..   Oscillation type,

Equalizer bar

No. of rollers:

Carrier roller..........................……………………………   2 each side

Track roller............................……………………………   7 each side

Shoe:

Type....................................……………………………..    Assembled, extreme

service shoes

Grouser height..........................………………………….   88 mm

No. of shoes............................……………………………….    39, each side

Pitch...................................………………………………   260.35 mm

Width...................................……………………………..   610 mm

POWER TAKE OFF:

# Location................................…………………………….   Right side of

Flywheel housing

Shaft revolutions.......................………………………….   1,726 RPM

Rotational direction....................…………………………  Clockwise (as

viewed from drive side)

COOLANT AND LUBRICANT CAPACITY:

Cooling water...........................…………………………..  180 ltr.

Fuel tank...............................……………………………..  750 ltr.

Engine..................................……………………………… 71 ltr.

Torque converter

Transmission…………………………………………….    230 ltr.

Bevel gear case

Steering case

Final drive case (each side)............……………………..      68 ltr.

Recoil spring case (each side)..........…………………….     30 ltr.

OTHERS

Material components for severe cold

Vandalism protection for fuel tank, hydraulic tank, radiator

Seat belt

Lighting (Front x 2, Rear x 1)

EXCLUSIVE ENGINE PREHEATER FOR D355A-3 TRACTOR

EQUIPMENT WEIGHT

(included to bare tractor)..............……………………….     60 kg

HEATER:

Type.....................................……………………………..     Combustion type heater

on board  a machine

Weight:

Heater body assembly ..................………………..    40 kg

Mounting and instrument panel ass'y ....................     20 kg

Performance:

Calorific value.....................………………………    30,000 kcal/h

Volume of blast.....................……………………..    480 c.m/h

Hot blast temperature elevation.....………………..   +250 o C

# Fuel consumption.....................……………………   3.5 ltr/h

Fuel oil............................…………………………. Cold-proof oil or kerosene

Electric power source ...............……………………  24 V D.C.

Power consumption:

# In operation...................…………………….  180 W

In preheating..................……………………  590 W (for about 1 min.)

Dimensions of the heater body:

Overall length.......................………………………   800 mm

Overall width........................………………………   320 mm

Overall height.......................………………………   355 mm

Objects of preheating....................…………………………   Engine oil pan

and radiator

Machine conditions:                                                                 Equipped with quilted

engine side covers and

radiator shutter kept

closed

Drawing.      DRAWBAR PULL VS. TRAVEL SPEED.

## KOMATSU D355A-3 STRAIGHT-TILT DOZER

## Specifications

EQUIPMENT WEIGHT

(Additional weight to bare tractor).....………………………  8710 kg

DIMENSIONS:

Length (Additional length

to overall length of bare tractor).......………………………..  1715 mm

Width...................................………………………………..   4315 mm

Ground pressure (Additional pressure

to bare tractor)........................………………………………   0.21 kg/cm2

DOZER EQUIPMENT:

Type....................................………………………………..   Straight, hydraulic tilting

Weight..................................……………………………….  7830 kg includes

cylinder support 1390 kg

Blade:

Length x height....................……………………….   4315 mm x 1875 mm

Digging angle......................……………………….    52 o

# Max. lift above ground...................………………………..   1545 mm

Max. drop below ground...................………………………    700 mm

Max. tilt adjustment....................…………………………..   1000 mm

HYDRAULIC CONTROL UNIT:

Weight..................................……………………………….    880 kg

Max. oil pressure.......................……………………………    140 kg/cm2

Hydraulic pump:

# Type...............................……………………………   Gear pump

Capacity (discharge flow)..........……………………   396 ltr/min at

engine 2.000 RPM

Location...........................…………………………..  Rear of engine right side

Control valve:

Type...............................……………………………   Spool type

Position:

Lifting............................……………………………   Raise, hold, lower

and float

Tilting............................……………………………   Left, hold and right

Hydraulic cylinder:

Type...............................……………………………   Double action,

piston type

No. of cylinders - bore:

Lift cylinder......................………………………….   2 - 160 mm

Tilt cylinder......................………………………….   1 - 250 mm

Hydraulic tank:

Type...............................……………………………   Equipped with

built-in control valve

Location...........................…………………………..   Right side of

operator's seat

Filter.............................…………………………….    Full flow type

Hydraulic oil......................…………………………   280 ltr.

KOMATSU D355A-3 GIANT RIPPER

(Single-shank ripper, variable)

## Specifications

EQUIPMENT WEIGHT

(Additional weight to bare tractor)..………………………     5440 kg

DIMENSIONS:

Length (Additional length to

overall bare tractor)....................………………………….     2510 mm

Overall width............................…………………………..      3030 mm

Ground pressure (Additional pressure

to bare tractor)........................…………………………….     0.13 kg/cm2

RIPPER EQUIPMENT:

Type....................................……………………………….     Variable digging

angle type

Weight..................................………………………………    5350 kg

Shanks:

No. of shanks...........................……………………………     1

Tooth point.............................…………………………….     Reversible

Digging angle................................………………………………..     45o STD

(available on stepless

adjustable ripper

between 37 10' - 61 20')

Digging depth...........................…………………………..      Adjustable to 4 stage

Max. digging depth......................………………………..      1400 mm

Max. lift above ground..................……………………….      1130 mm

Hydraulic cylinder:

Type....................................………………………………      Double acting,

piston type

No. of cylinders - bore x stroke:

Lift cylinder...........................…………………………….      2 - 225mm x 600mm

Tilt cylinder...........................……………………………..     2 - 225mm x 500mm

HYDRAULIC CONTROL UNIT:

Weight..................................………………………………      90 kg

Max. oil pressure.......................……………………………   140 kg/cm2

Hydraulic pump:

Type....................................…………………………………  Gear pump

Capacity (discharge flow)...............………………………..    396 ltr/min.

at engine 2000 RPM

# Location................................………………………………    Rear of engine

right side

Control valve:

Type....................................………………………………..    Spool type

Position................................………………………………     Raise, hold and lower

Hydraulic tank..........................……………………………     Equipped with

built-in control valve

Location................................………………………………     Right side of

operator's seat

Hydraulic oil...........................……………………………..     100 ltr.

Selector valve:

Type....................................…………………………………   Spool type

Position................................………………………………..    Lift cylinder and

tilt cylinder

Location................................………………………………     Rear of steering case

PIN PULLER EQUIPMENT:

Max. oil pressure.......................……………………………    20 kg/cm2

Hydraulic cylinder:

Type....................................…………………………………   Double acting,

piston type

No. of cylinders - bore x stroke........………………………..  1 - 70mm x 160mm

Control valve:

Type....................................…………………………………   Spool type

Position................................………………………………..    Pull, hold and push

KOMATSU D355A-3 ROPS TYPE STEEL CAB

Specifications

# EQUIPMENT WEIGHT.............................…………………………  2,450 kg

(Additional weight to bare tractor)

DIMENSIONS:

Ground pressure.........................…………………………….  0,06 kg/cm2

(Additional pressure to bare tractor)

STEEL CAB: (Window glass: double type)

Type....................................…………………………………   4 column ROPS type

all steel, enclosed type

Weight..................................………………………………..   2,450 kg

Length..................................………………………………..    2,925 mm

Width...................................………………………………..    1,990 mm

Height (floor to roof)..................……………………………   1,930 mm

Roof dimensions:

Length..................................………………………………..    2,380 mm

Width...................................……………………………….     1,600 mm

Area....................................…………………………………    3.81 sq. m

Thickness................................………………………………    3.2 mm

ACCESSORY:

Wiper..................................………………….      4

Room lamp...............................……………….    1

Floor mat...............................…………………    1 set

Inner lining for ceiling...............………………    1 set

OPTION:

Heater hot water type...................………………  4,000 kcal/h x 2  + 4,000 kcal/h x 2

Ventilator..............................…………………..   1

Operation lamp..........................………………..   4 (front x 2,  rear x 2)

Inspection lamp.........................………………..   1

Fire extinguisher......................…………………  1

First-aid box.........................……………………  1

Ash tray................................……………………  1

# Cigarette lighter...................……………………  1

# Water bottle..........................…………………… 1

Sunvisor...............................……………………  1

Rear view mirror.......................………………..   1

KOMATSU D355A-3 TRACTOR (-50oC Specification)

STANDARD TOOL TABLE

Part No.		Part Name			          Q-ty	Remarks

0900-30006		WRENCH SET			1S	 8x10, 12x14, 13x17,

19x22, 24x27, 30x32

09020-10284		SOCKET WRENCH SET		1S	10,13,14,17,22,24,

27,30,32,36

09030-00150		SCREW DRIVER			1

09036-00150		PLIERS				1

09039-00150		HAMMER				1

09040-00800		OILER			                        1

09055-00520		PINCH BAR				1

07952-80001		GREASE PUMP			1

07951-11400		NOZZLE (B)			            1

195-98-11590	           SOCKET				1	41

09033-00190		SCREW DRIVER			1

09029-00450		PINCH BAR			            1

09002-03236		WRENCH				1	32X36

09002-04146		WRENCH				1	41X46

07950-90401		CARTRIDGE			            1

09007-00528		WRENCH				1

09019-08035		WRENCH				1

KOMATSU D355A-3 TRACTOR (-50oC Specification)

STANDARD SPARE PARTS TABLE

Parts No.                     Parts Name	Q-ty	 REMARKS

175-49-11580	            ELEMENT	 3	 For steering and transmission

07063-01142		ELEMENT	 1	 For hydraulic filter

07000-42110		O-RING	 3	 For steering filter

07000-42115		O-RING	 3	 For transmission filter

07000-45175		O-RING	 1	 For hydraulic filter

07000-43032		O-RING	 4	 For steering case and final case drain

07020-00000		GREASE-

FITTING	 4

07020-00675		GREASE-

FITTING	 4

07020-00900		GREASE-

FITTING	 4

195-98-13440	            PLUG SET	 1

600-211-1290	            CARTRIDGE  4	For engine oil filter

6610-51-5300	            ELEMENT	 1	For engine by-pass filter

02892-43021		O-RING	 1	For engine by-pass filter

02894-47201		O-RING	 1	For engine by-pass filter

600-311-8281	            CARTRIDGE  2	For engine fuel filter

6127-11-8812	            GASKET	 3	For cylinder head cover

6127-11-7811	            GASKET         3	For rocker housing

04122-32564		V-BELT	 1	For fan drive

600-736-9390	            V-BELT	 1	For alternator drive

KOMATSU D355A-3 TRACTOR (-50oC specification)

ACCESSORY TABLE

Part No.		Part name		                  Q-ty		Remarks

09056-08015		TOOL BAG			        1

TOOL AND ACCES SORY

TABLE		                    1

09980-10550		WORKING DRESS		        1

09982-10057		WORKING CAP		        1

PARTS BOOK		        1

# OPERATIONAL MANUAL          1

STARTING SWITCH  KEY	        2

195-98-11259	             SPARE PARTS TABLE               1

09059-00800		 SPARE PARTS BOX                    1

175-900-2470	             INSPECTION LAMP                    1

195-60-19300	             HOSE				         1