KOMATSU

BULLDOZER

D275A-5

WITH

SEMI-U TILT DOZER

GIANT RIPPER

ROPS CANOPY & STEEL CAB

HEATER & DEFROSTER

FOR  -50ОС  ~  +40ОС  OPERATION

KOMATSU D275A-5 TRACTOR

Specification

| Operating weight | 37,680 кг |
| --- | --- |
| Flywheel horsepower SAE J1349 DIN (6270) | 306 kW (410 HP)/ 2000 rpm 306 kW (416 PS)/ 2000 rpm |
| PERFOMANCE: |  |
| Travel speed and drawbar pull: Forward 1st 2nd 3rd Revers 1st 2nd 3rd | 3.8 km/h 6.7 km/h 11.2 km/h 4.9 km/h 8.7 km/h 14.9 km/h |
| Turning radius | 3.9 m |
| DIMENSIONS: |  |
| Overall length | 5,255 mm |
| Overall width | 2,925 mm |
| Overall height |  |
| To top of exhaust pipe | 3,965 mm |
| Highest point, exclusive of exhaust pipe | 3,070 mm To top of aircleaner |
| Track gauge | 2,260 mm |
| Length of track on ground | 3,480 mm |
| Ground contact area | 42,456 см2 |
| Ground pressure | 0.89 kgf/см2 |
| Ground clearance | 507 mm |
| ENGINE: |  |
| Model | KOMATSU SDA6D140 |
| Type | Water cooled, 4-cycle, direct injection, turbocharged and aftercooled diesel engine |
| No. Of cylinders – bore x stroke | 6 - 140 mm х 165 mm |
| Piston displacement | 15.24 ltr. |
| Performance: |  |
| Max. torque | 2000 rpm |
| Engine rpm at max. torque | 207 kgf.m/1400 prm |
| Flywheel horsepower SAE J1349 DIN (6270) | 410 HP/ 2000 rpm 416 PS/ 2000 rpm |

| Fuel system: Fuel Governor type | Diesel gas oil, ASTM Specification D975060T No.2D Electronic, all-speed control |
| --- | --- |
| Lubrication system: Lubrication method Lubrication filter Cooling method | Gear pump, forced lubrication Full-flow Water cooled |
| Cooling system: Cooling method Fan type | Forced circulation by centrifugal water pump Pusher type fan |
| Air cleaner | Dry type with automatic dust evacuator and dust indicator |
| Starting system: Starting method Starting motor Alternator Battery | By electric starting motor 24 V, 22 kW (11 kW x 2) 24 V, 75 A 24 V (12 V x 2) – 200 Ah |
| Starting Aid |  |
| Combustion type coolant pre-heater | 26,000 kcal/h |
| Combustion type hot-air pre-heater | 30,000 kcal/h |
| Engine side cover | Closed type |
| Battery warmer | Hot water type Battery box with felt lining |
| POWER TRANSMITTING SYSTEM: |  |
| Torque converter: |  |
| Type | 3-element, single-stage, single-phase |
| Cooling method | Water cooling |
| TRANSMISSION: |  |
| Type | Planetary gear and multiple-disc clutch, hydraulically actuated, forced lubrication |
| Gear shift | 3 forward and 3 reverse speed |
| Bevel gear | Spiral bevel gear, splash lubrication |
| Steering system: |  |
| Steering clutch | Wet, multiple-disc clutch, hydraulically released, hand operated, interconnected with steering brake |
| Steering brake | Wet, multiple-disc, spring actuated, hydraulically released, pedal/lever operated |
| Service brace | Steering brakes function as service brake, foot operated |
| Final drive | Spur gear and planetary |
| UNDERCARRIGE: |  |
| Suspension | Oscillation type, equalizer bar |
| No of rollers: |  |
| Carrier rollers | 2, each side |
| Track rollers | 7, each side |
| Track shoe assembly: |  |
| Type | Assembled, lubricated and sealed track |
| Pitch | 260.35 mm |
| Track shoe: |  |
| Type | Single grouser |
| Standart shoe width | 610 mm |
| Grouser height | 88 mm |
| No. of shoes | 39, each side |
| SERVICE REFILL CAPACITIES: |  |
|  | Specified | Refilled |
| Coolant | 130 ltr | 130 ltr |
| Fuel tank | 840 ltr | 840 ltr |
| Engine | 55 ltr | 52 ltr |
| Damper | 1.5 ltr | 1.5 ltr |
| Torque converter, Transmission, Bevel gear case, Steering case | 150 ltr | 90 ltr |
| Final drive case, each side | 40 ltr | 40 ltr |

KOMATSU D275A-5 SEMI-U-DOZER

SPECIFICATIONS

| EQUIPMENT WEIGHT (Additional weight to tractor) |  |
| --- | --- |
| Standard blade | 7 507 kg |
| DIMENSION: |  |
| Length (Additional length to tractor) | 1675 mm |
| Overall width | 4300 mm |
| Ground pressure (Additional pressure to tractor) | 0.18 kg/cm2 |
| DOZER EQUIPMENT: |  |
| Type | Semi-U blade, hydraulically tilting |
| Blade: |  |
| Weight standard blade | 7507 kg Including blade support 728 kg |
| Blade capacity(SAE) | 13,7 m3 |
| Blade support method | Brace support type |
| Length | 4300 mm |
| Height | 1960 mm |
| Digging angle | 52 deg. |
| Max. lift above ground | 1450 mm |
| Max. drop below ground | 640 mm |
| Max. tilt adjustment | 1000 mm |
| HYDRAULIC CYLINDERS: |  |
| Type | Double-acting, piston type |
| No. of cylinders – bore: Lifting cylinder Tilting cylinder | 2 – 120 mm 1 – 180 mm |
| HYDRAULIC EQUIPMENT: |  |
| Additional hydraulic oil weight | 29 kg |
| Max. oil pressure | 280 kg/cm2 |
| Hydraulic pump: |  |
| Type | Plunger pump |
| Capacity (discharge flow) | 230 ltr./min at engine rated rpm |
| Location | Rear of engine right side |
| Control valve | Spool type |
| Position |  |
| Lifting spool Tilting spool | Raise, hold, lower and float Right, hold and left |
| Hydraulic tank: |  |
| Type | Equipment with externally-mounted control valve |
| Location | Right of operator`s seat |
| Filter | Full-flow type |
| Hydraulic oil (Refilled) | 130 ltr |

KOMATSU D275A-5 GIANT RIPPER

(Variable digging angle type)

Specifications

| EQUIPMENT WEIGH: |  |
| --- | --- |
| (additional weight to tractor) | 4600 kg |
| DIMENSION: |  |
| Length (additional Length to tractor) | 2360 mm |
| Ground pressure to tractor (Additional pressure to tractor) | 0.11 kg/сm2 |
| RIPPER EQUIPMENT: |  |
| Type | Parallelogram, variable digging angle type |
| Weight | 3849 kg |
| Beam lenght | 1252 mm |
| Shanks: |  |
| No. of shanks | 1 |
| Tooth point | Replaceable |
| Digging angle | 52.7 deg., STD. (available stepless angle adjustment) |
| Max. digging depth | 1420 mm |
| Max. lift above ground | 1195 mm |
| Hydraulic cylinders: |  |
| Type | Double-acting, piston type |
| No. of cylinders – bore: |  |
| Lifting cylinder | 2 - 180 mm |
| Tilting cylinder | 2 - 160 mm |
| HYDRAULIC EQUIPMENT: |  |
| Max. oil pressure | 280 kgf/cm2 |
| Hydraulic pump: |  |
| Type | Plunger pump |
| Capacity (discharge flow) | 230 ltr./ min at engine rated rpm |
| Location | Rear of engine right side |
| Control valve: |  |
| Тype | Spool type |
| Position: |  |
| Lifting cylinder | Raise, hold, lower and float |
| Tilting cylinder | Digging angle increase, hold and decrease |

| Note: Lifting spool and tilting spool are change-overed with selector valve. |
| --- |
| Hydraulic tank: |  |
| Тype | Equipped with externally-mounted control valve |
| Location | Right of operator`s seat |
| Filter | Full-flow type |
| Hydraulic oil | 130 ltr. |

KOMATSU  D275A-5 ROPS CANOPY

Specifications

| EQUIPMENT WEIGH: |  |
| --- | --- |
| (Additional weight to tractor) | 650 kg |
| DIMENSION: |  |
| Ground pressure (Additional pressure to tractor) | 0.02 kgf/cm2 |
| ROPS CANOPY |  |
| Type | 2-column ROPS canopy |
| Weight | 650 kg |
| Length | 1405 mm |
| Width | 2035 mm |
| Roof area | 2.30 m2 |
| Plate thickness | 4.5 mm |

Structure and strength comply with ROPS ISO 3471, SAE J1040 (April, 88), SAE J395 and ISO 3449 FOPS standards.

KOMATSU D275A-5 STEEL CAB

Specifications

| EQUIPMENT WEIGH: |  |
| --- | --- |
| (Additional weight to tractor) | 490 kg |
| DIMENSION: |  |
| Ground pressure (Additional pressure to tractor) | 0.01 kg/см2 |
| STEEL CAB |  |
| Type | All weather, enclosed type |
| Weight | 490 kg |
| Length | 1790 mm |
| Width | 1455 mm |
| Height: |  |
| Floor mat to ceiling | 1530 mm |
| HEATER | 5000 kcal/h x 1 4000 kcal/h x 1 |

| STANDARD EQUIPMENT: |  |
| --- | --- |
| Wiper | 4 (2 front & 2 rear) |
| Lamp | 1 |
| Rear view window | 1 |
| Ash tray, cigarette lighter | 1 |
| Floor mat | 1 |

KOMATSU D275A-5 TRACTOR

###### ACCESSORY PARTS TABLE

| Part No. | Part Name | Q`ty | Remarks |
| --- | --- | --- | --- |
|  | STARTING SWITCH KEY | 2 |  |
|  | PARTS BOOK | 1 |  |
|  | OPERATION & MAINTENANCE | 1 |  |

| TOOL TABLE |
| --- |
| Part No. | Part Name | Q`ty | Remarks |
| 09000-30006 | Wrench set | 1 |  |
| 09020-10284 | Socket Wrench | 1 |  |
| 09022-00150 | Extension | 1 |  |
| 09022-00250 | Extension | 1 |  |
| 09023-00300 | Handle | 1 |  |
| 09024-00300 | Handle | 1 |  |
| 09026-00250 | Handle | 1 |  |
| 09025-00075 | Joint | 1 |  |
| 09027-00300 | Bar | 1 |  |
| 09033-00190 | Driver | 1 |  |
| 09036-00150 | Pliers | 1 |  |
| 09039-00150 | Hammer | 1 |  |
| 09040-00800 | Lubricator | 1 |  |
| 07952-70004 | Pump | 1 |  |
| 07951-11400 | Nozzle | 1 |  |
| 09055-10390 | Bar Pinch | 1 |  |
| 09002-03641 | Wrench | 1 |  |
| 09001-04600 | Wrench | 1 |  |
| 09019-08035 | Wrench | 1 |  |
| 07950-90403 | Cartridge | 1 |  |
| 09056-05513 | Bag | 1 |  |
| 09054-00009 | Gauge | 1 |  |

| KOMATSU D275A-5 TRACTOR |
| --- |
| SPARE PARTS TABLE |
| Part No. | Part Name | Q`ty | Remarks |
| 09980-10550 | Overall | 1 |  |
| 09982-10057 | Cap | 1 |  |
| 09059-00800 | Spare parts box | 1 |  |
| 07063-01100 | Element | 2 |  |
| 20Y-60-31121 | Element | 1 |  |
| 07000-12130 | O-ring | 2 |  |
| 07000-15195 | O-ring | 1 |  |
| 07000-12110 | O-ring | 1 |  |
| 07002-03634 | O-ring | 6 |  |
| 07002-02034 | O-ring | 1 |  |
| 07020-00000 | Fitting | 4 |  |
| 07020-00675 | Fitting | 4 |  |
| 07020-00900 | Socket | 4 |  |
| 6212-85-6840 | V-belt | 1 |  |
| 6217-11-8820 | Gasket | 6 |  |
| 600-21-11340 | Cartridge | 1 |  |
| 600-31-13110 | Cartridge | 1 |  |