KOMATSU D355C-3

# PIPELAYER

## WITH STEEL CAB

SHOE WIDTH:      860 mm

BOOM LENGTH:  8,560 mm

### FOR

ATMOSPHERIC TEMPERATURE:

FROM - 30C  UP TO +40 C

(SPECIFICATIONS ARE SUBJECT TO CHANGE WITHOUT NOTICE)

GENERAL SPECIFICATIONS

OPERATING WEIGHT:-----------------------------------------------------------58,2000kg

DIMENSIONS:

Overall length-------------------------------------------------------------6,030 mm

Overall width--------------------------------------------------------------4,405 mm

(exclusive of  boom, counterweight retracted )

Overall height:------------------------------------------------------------4,020 mm

Ground Pressure-----------------------------------------------------------0.90 kg/sq.sm

CONTAINS:

1 D355C PIPELAYER SPECIFICATIONS

2 D355C STEEL CAB SPECIFICATIONS

3 STANDARD TOOL, SPARE PARTS and ACCESSORY TABLE

KOMATSU D355C-3 PIPELAYER

SPECIFICATIONS:

| OPERATING WEIGHT | 57,530 kg |
| --- | --- |
| SHIPPING WEIGHT (chassis only) | 40,580 kg |
| MAX. LIFTING CAPACITY | 117 ton.m (at 2.5m) |
| FLYWHEEL HORSEPOWER | 360 HP |
| DIMENSIONS: |  |
| Overall length | 6,030mm |
| Overall width: |  |
| Width counterweight retracted | 4,405 mm |
| Shipping width | 3,410 mm |
| (boom, frames, counterweight, steps, removed) |  |
| Overall height: |  |
| To top of rain cap | 3,925 mm |
| To highest point, exclusive of exhaust pipe, boom, cabin, frame of right and left side counterweight (To top of winch) | 3,020 mm |
| Truck gauge | 2,550 mm |
| Length of truck on ground | 3,750 mm |
| Ground contact area | 64,500 sq.cm |
| Ground pressure | 0.90 kg/sq.sm |
| Ground clearance | 635 mm |
| PERFORMANCE: |  |
| Travel speed: |  |
| Forward 1-st | 0 - 3.3 km/h |
| 2-nd | 0 - 5.9 km/h |
| 3-rd | 0 - 9.8 km/h |
| Reverse 1-st | 0 - 3.9 km/h |
| 2-nd | 0 - 7.0 km/h |
| 3-rd | 0 - 11.0 km/h |
| PIPELAYER EQUIPMENT: |  |
| Lifting performance | Refer to the attached sheet, according to ANSI and SAE |
| Boom overhang | 1.3 - 8.5 m |
| Hook speed: (bare Drum) |  |
| Raise: |  |
| Low | 5.5 m/min |
| High | 12.7 m/min |
| Lower: |  |
| Low | 4.5 m/min |
| High | 10.2 m/min |
| Boom: |  |
| Type | Box section and be operated by wire ropes |
| Boom equipment: |  |
| Boom length | 8,560 mm |
| Weight | 2,520 kg |
| Winch equipment |  |
| Type | Hydraulically controlled, double drum reversible |
| Driving system | Hydroshift, wet multiple disc clutch type |
| Brake | Hydraulicaly released, spring applied wet multiple disc clutch type |
| Transmission | Wet multiple disc clutch type, in high-low range |
| Winch drum: |  |
| Hook (dia x width) | 290mm x 340mm |
| Boom (dia x width) | 290mm x 166mm |
| Wire rope: |  |
| Hook (dia x length) | 20mm x 105mm |
| Boom (dia x length) | 20mm x 65mm |
| Weight | 3,310 kg |
| Counterweight equipment: |  |
| Type | Segment plate type, hydraulically controlled |
| Weight per plate | 1530 kg |
| No of plate | 6 |
| Oil pressure | 140 kg/sq.sm |
| Weight including frame, link Assy, cylinder and weight plate | 12,900 kg |
| Safety equipment: |  |
| Boom | Automatic maximum stopper device |
| Winch and sheave | Automatic overwind stopper device |
| Boom | Indicator for radius and permissible lifting load |
| Hook | With safety lock |

| Moment limiter | Automatic overload limiter device 87% |
| --- | --- |
| ENGINE: |  |
| Model | KOMATSU S6D140-2 |
| Type | Water cooled, 4-cycle, in-line, vertical type, direct injection type, turbocharged, after cooler, diesel engine |
| No of cylinders - bore x stroke | 6 - 140mm x 165mm |
| Piston displacement | 15,240 cc |
| Performance |  |
| Rated RPM | 2000RPM |
| Flywheel horsepower | 360HP |
| Max.torque | 160kg.m/1400RPM |
| Fuel System: |  |
| Fuel oil | According to Komatsu recommendation |
| Governor | Mechanical, all speed control |
| Lubrication System: |  |
| Lubricating method | Gear pump, forced lubrication |
| Filter | Full-flow and by-pass type |
| Oil cooler | Water cooled |
| Cooling system | Forced circulation, by centrifugal water pump, reversible fan |
| Air cleaner | Dry type with automatic dust ejector and dust indicator |
| Starting method | By electrical starting motor 24V, 22KW (11kwx2) |
| Staring aid: |  |
| Combustion type coolant, oil pan | 30,000 Kcal/h |
| Intake air heater (electric type) | 24V, 5,7 KW |
| Coolant heater (electric type) | 230V, 1.5KWx1 |
| Oil pan heater (electric type) | 230V, 0.6KWx1 |
| Battery warmer | Hot air type battery box with left lining |
| Engine side cover | Closed type |
| Radiator shutter | Metal type, operated from cabin room |
| Alternator | 24V, 50A |
| Battery | 24V (12Vx4)-200Ah |
| Portable combustion type heater | 30,000 Kcal/h x 1 |
| POWER TRANSMITTING SYSTEM: |  |
| Torque converter: |  |
| Type | 3 element, single stage and single phase |
| Cooling method | Water cooled |
| Transmission: |  |
| Type | Planetary gear and multiple disc clutch, hydraulically actuated, forced lubrication |
| Gear shift | 3 forward nd 3 reverse speeds |
| Bevel gear | Spiral bevel gear |
| Steering system: |  |
| Steering clutch | Wet multiple disc, spring loaded, band operated, Hydraulically actuated |
| Steering brake | Wet, contracting band, foot operated, interconnected with steering clutch, with hydraulic booster |
| Final drive | Spur gear single reduction and planetary gear single reduction |
| UNDERCARRIAGE: |  |
| Suspension | Non-oscillating type |
| No of rollers: |  |
| Carrier roller | 2, each side |
| Track roller | 8, each side |
| Shoe: |  |
| Type | Assembled single grouser |
| Grouser height | 88mm |
| No of shoes | 42, each side |
| Pitch | 260.35mm |
| Width | 860mm |
| DRAWBAR |  |
| Type | Fixed type drawbar |
| Height of drawbar above ground (Exclusive of grouser height) | 640mm |
| POWER TAKE OFF: |  |
| Location | Rear of engine |
| Shaft revolutions | 1725 RPM at engine 2000RPM |
| Rotational direction | Clockwise (as viewed from drive side) |
| COOLANT AND LUBRICANT CAPACITY: |  |
| Coolant water | 145ltr |
| Fuel tank | 640ltr |
| Engine | 42ltr |
| Torque converter Transmission Bevel gear case Steering case | 230ltr |
| Final drive case | 68ltr |
| Winch case | 125ltr |
| Counterweight tank | 47ltr |
| Others: Vandalism protection for fuel tank, hydraulic tank, radiator |  |

| KOMATSU D355C-3 STEEL CAB Specifications |
| --- |
| EQUIPMENT WEIGHT (Additional weight to bare-tractor) | 750kg |
| DIMENSIONS: |  |
| Overall height | 4020mm |
| Ground pressure (Additional pressure to bare tractor) | 0.01kg/sq.sm |
| STEEL CAB (Window glass: single type) |  |
| Cab heater | 5400kcal/h x 1 |
| Type | All steel, enclosed type |
| Weight | 670kg |
| Length | 2070mm |
| Width | 1785mm |
| Height (Floor to ceiling) | 1460mm |
| ACCESSORY: |  |
| Wiper | 2 (Front and rear) |
| Room lamp | 1 |
| Ventilator | 1 |
| Rear lamp | 2 |
| Floor mat | 1 set |
| Heater (hot water type including defroster) | 5400Kcal/hx1 |
| Inspection lamp | 1 |
| Sunvisor | 1 |
| Fog lamp | 1 |
| Fire extinguisher | 1 |
| First aid box | 1 |
| Water bottle | 1 |
| Ash tray, cigarette lighter | 1 |
| Rear view mirror | 1 |
| Working light (for boom) | 1 |
| Winch lamp | 1 |

KOMATSU D355C-3 PIPELAYER LIFTING PERFORMANCE CURVE

Lifting load performance curve Boom length 8560 mm

Wirerope for hook Diameter 20 mm

Wirre cutting load 27, 600 kg

Wirerope for boom Diameter 20 mm

Wirre cutting load 27, 600 kg

- 8 part hook line

- 5 part book line

- Weight of counterweight plate 12,900 kg - Lifting performance is shown with counterweight extended

BOOM OVERHANG (L)

KOMATSU D355C-3 PIPELAYER DRAWBAR PULL VS TRAVEL SPEED

Note: The drawbar pull travel speed may be subject to change depending on the graund conditions and machine weight.

| KOMATSU D355C-3 PIPELAYER STANDARD TOOL TABLE |
| --- |
| Parts No | Parts Name | Qty | Remarks |
| 09000-30006 | WRENCH | 1 SET | 8x10, 12x14, 13x17, 19x22, 24x27, 30x32 |
| 09020-10284 | SOCKET WRENCH SET | 1 SET | 10. 12. 13. 14. 17. 19. 22. 24. 27. 30. 32, 36 |
| 09033-00190 | SCREW DRIVER | 1 |  |
| 09036-00150 | PLIERS | 1 |  |
| 09039-00150 | HAMMER | 1 |  |
| 07952-80002 | GREASE PUMP | 1 |  |
| 07951-11400 | NOZZLE | 1 |  |
| 07950-90403 | CARTRIDGE | 1 |  |
| 09054-00009 | THICKNESS GAUGE | 1 |  |
| 09055-10390 | PINCH BAR | 1 |  |
| 09002-03641 | WRENCH | 1 | 36, for winch rubber hose |
| 09001-04600 | WRENCH | 1 | for winch cooler rubber hose |
| 09019-08035 | WRENCH | 1 | for engine filter |
| 09056-05513 | TOOL BAG | 1 |  |
| 175-900-3910 | LEVER ASS’Y | 1 | Only for over turning Reversible fan (Option) |
| 196-98-21190 | WRENCH | 1 | Only for Towing winch (Option) |

| KOMATSU D355C-3 PIPELAYER STANDARD SPARE PARTS TABLE |
| --- |
| PARTS No | PARTS NAME | QTY | REMARKS |
| 175-49-11850 | ELEMENT | 2 | For steering oil filter |
| 07000-03120 | O-RING | 2 | For steering oil filter |
| 175-49-11580 | ELEMENT | 1 | For transmission oil filter |
| 07000-02115 | O-RING | 1 | For transmission oil filter |
| 130-60-48210 | ELEMENT | 1 | For counterweight oil filter |
| 07000-03078 | O-RING | 1 | For counterweight oil filter |
| 144-60-11160 | ELEMENT | 1 | For winch oil filter |
| 07000-02115 | O-RING | 1 | For winch oil filter |
| 07020-00000 | FITTING | 4 |  |
| 07020-00675 | FITTING | 4 |  |
| 07020-00900 | FITTING | 4 |  |
| 07000-03032 | O-RING | 1 | For torque converter oil drain |
| 07002-03634 | O-RING | 1 | For steering case oil drain |
| 07002-03634 | O-RING | 2 | For final drive case oil drain |
| 07002-04234 | O-RING | 2 | For final drive case inlet port |
| 07002-02434 | O-RING | 1 | For counterweight oil drain |
| 07002-02434 | O-RING | 1 | For winch level gauge |
| 07002-04234 | O-RING | 1 | For winch inlet port |
| 600-211-1231 | CARTRIDGE | 1 | For engine oil filter |
| 600-311-7132 | CARTRIDGE | 1 | For engine fuel filter |
| 04122-22575 | V-BELT | 1 | For fan drive |
| 6212-85-6840 | V-BELT | 1 | For alternator |
| 6210-11-8820 | GASKET | 6 | For cylinder head cover |
| 09059-00800 | BOX | 1 | For spare parts |

| KOMATSU D355C-3 PIPELAYER ACCESSORY PARTS TABLE |
| --- |
| PARTS No | PARTS NAME | QTY | REMARKS |
|  | SPARE PARTS TABLE | 1 |  |
|  | PARTS BOOK | 1 |  |
|  | OPERATION MANUAL | 1 |  |
| 09980-10550 | OVERALL | 1 |  |
| 09982-10057 | WORK CAP | 1 |  |
|  | STARTING SWITCH KEY | 2 |  |