KOMATSU D355C-3

# PIPELAYER

## WITH STEEL CAB

SHOE WIDTH:      860 mm

BOOM LENGTH:  8,560 mm

### FOR

ATMOSPHERIC TEMPERATURE:

FROM -50 C  UP TO +40 C

(SPECIFICATIONS ARE SUBJECT TO CHANGE WITHOUT NOTICE)

GENERAL SPECIFICATIONS

OPERATING WEIGHT:-----------------------------------------------------------59,550kg

DIMENSIONS:

Overall length-------------------------------------------------------------6,030 mm

Overall width--------------------------------------------------------------4,405 mm

(exclusive of  boom, counterweight retracted )

Overall height:------------------------------------------------------------4,020 mm

Ground Pressure-----------------------------------------------------------0.92 kg/sq.sm

CONTAINS:

1 D355C PIPELAYER SPECIFICATIONS

2 D355C STEEL CAB SPECIFICATIONS

3 STANDARD TOOL, SPARE PARTS and ACCESSORY TABLE

KOMATSU D355C-3 PIPELAYER

SPECIFICATIONS:

| OPERATING WEIGHT | 58,800 kg |
| --- | --- |
| SHIPPING WEIGHT (chassis only) | 41,100 kg |
| MAX. LIFTING CAPACITY | 117 ton.m (at 2.5m) |
| FLYWHEEL HORSEPOWER | 360 HP |
| DIMENSIONS: |  |
| Overall length | 6,030mm |
| Overall width: |  |
| Width counterweight retracted | 4,405 mm |
| Shipping width | 3,410 mm |
| (boom, frames, counterweight, steps, removed) |  |
| Overall height: |  |
| To highest point (cab light) | 4020 mm |
| To top of rain cap | 3,925 mm |
| To highest point, exclusive of exhaust pipe, boom, cabin, frame of right and left side counterweight (To top of winch) | 3,020 mm |
| Truck gauge | 2,550 mm |
| Length of truck on ground | 3,750 mm |
| Ground contact area | 64,500 sq.cm |
| Ground pressure | 0.91 kg/sq.sm |
| Ground clearance | 635 mm |
| PERFORMANCE: |  |
| Travel speed: |  |
| Forward 1-st | 0 - 3.3 km/h |
| 2-nd | 0 - 5.9 km/h |
| 3-rd | 0 - 9.8 km/h |
| Reverse 1-st | 0 - 3.9 km/h |
| 2-nd | 0 - 7.0 km/h |
| 3-rd | 0 - 11.0 km/h |
| PIPELAYER EQUIPMENT: |  |
| Lifting performance | Refer to the attached sheet, according to ANSI and SAE |
| Boom overhang | 1.3 - 8.5 m |
| Hook speed: (bare Drum) |  |
| Raise: |  |
| Low | 5.5 m/min |
| High | 12.7 m/min |
| Lower: |  |
| Low | 4.5 m/min |
| High | 10.2 m/min |
| Boom: |  |
| Type | Box section and be operated by wire ropes |
| Boom equipment: |  |
| Boom length | 8560 mm |
| Weight | 2,520 kg |
| Winch equipment |  |
| Type | Hydraulically controlled, double drum reversible |
| Driving system | Hydroshift, wet multiple disc clutch type |
| Brake | Hydraulicaly released, spring applied wet multiple disc clutch type |
| Transmission | Wet multiple disc clutch type, in high-low range |
| Winch drum: |  |
| Hook (dia x width) | 290mm x 340mm |
| Boom (dia x width) | 290mm x 166mm |
| Wire rope: |  |
| Hook (dia x length) | 20mm x 105mm |
| Boom (dia x length) | 20mm x 65mm |
| Weight | 3,310 kg |
| Counterweight equipment: |  |
| Type | Segment plate type, hydraulically controlled |
| Weight per plate | 1530 kg |
| No of plate | 6 |
| Oil pressure | 140 kg/sq.sm |
| Weight including frame, link Assy, cylinder and weight plate | 12,900 kg |
| Safety equipment: |  |
| Boom | Automatic maximum stopper device |
| Winch and sheave | Automatic overwind stopper device |
| Boom | Indicator for load and moment |
| Hook | With safety lock |

| Moment limiter | Automatic overload limiter device 87% |
| --- | --- |
| Engine: |  |
| Model | KOMATSU S6D140-2 |
| Type | Water cooled, 4-cycle, in-line, vertical type, direct injection type, turbocharged, diesel engine |
| No of cylinders - bore x stroke | 6 - 140mm x 165mm |
| Piston displacement | 15,240 cc |
| Performance |  |
| Rated RPM | 2000RPM |
| Flywheel horsepower | 360HP |
| Max.torque | 160kg.m/1400RPM |
| Fuel System: |  |
| Fuel oil | According to Komatsu recommendation |
| Governor | Mechanical, all speed control |
| Lubrication System: |  |
| Lubricating method | Gear pump, forced lubrication |
| Filter | Full-flow |
| Oil cooler | Water cooled |
| Cooling system | Forced circulation, by centrifugal water pump, reversible fan |
| Air cleaner | Dry type with automatic dust ejector and dust indicator |
| Starting method | By electrical starting motor 24V, 22KW (11kwx2) |
| Staring aid: |  |
| Combustion type coolant, oil pan heater | 30,000 Kcal/h |
| Intake air heater (electric type) | 24V, 5,7 KW |
| Coolant heater (electric type) | 230V, 1.5KWx1 (option) |
| Oil pan heater (electric type) | 230V, 0.6KWx1 (option) |
| Battery warmer | Hot air type battery box with left lining |
| Engine side cover | Closed type |
| Automatic priming system: |  |
| Air intake system from bonnet inside port |  |
| Radiator shutter | Metal type, operated from cabin room |
| Engine room quilting | Cloth type (option) |
| Alternator | 24V, 50A |
| Battery | 24V (12Vx2)-200Ah |
| Portable combustion type heater | 30,000 Kcal/h x 1 (option) |
| POWER TRANSMITTING SYSTEM: |  |
| Torque converter: |  |
| Type | 3 element, single stage and single phase |
| Cooling method | Water cooled |
| Transmission: |  |
| Type | Planetary gear and multiple disc clutch, hydraulically actuated, forced lubrication |
| Gear shift | 3 forward nd 3 reverse speeds |
| Bevel gear | Spiral bevel gear |
| Steering system: |  |
| Steering clutch | Wet multiple disc, spring loaded, band operated, Hydraulically actuated |
| Steering brake | Wet, contracting band, foot operated, interconnected with steering clutch, with hydraulic booster |
| Final drive | Spur gear single reduction and planetary gear single reduction |
| UNDERCARRIAGE: |  |
| Suspension | Non-oscillating type |
| No of rollers: |  |
| Carrier roller | 2, each side |
| Track roller | 8, each side |
| Shoe: |  |
| Type | Assembled single grouser |
| Grouser height | 88mm |
| No of shoes | 42, each side |
| Pitch | 260.35mm |
| Width | 860mm |
| DRAWBAR |  |
| Type | Fixed type drawbar |
| Height of drawbar above ground (Exclusive of grouser height) | 640mm |
| POWER TAKE OFF: |  |
| Location | Rear of engine |
| Shaft revolutions | 1725 RPM at engine 2000RPM |
| Rotational direction | Clockwise (as viewed from drive side) |
| COOLANT AND LUBRICANT CAPACITY: |  |
| Coolant water | 145ltr |
| Fuel tank | 640ltr |
| Engine | 42ltr |
| Torque converter Transmission Bevel gear case Steering case | 230ltr |
| Final drive case | 68ltr |
| Winch case | 125ltr |
| Counterweight tank | 47ltr |
| Combustion preheater fuel tank | 12ltr |
| Others: Material components for severe cold. Vandalism protection for fuel tank, hydraulic tank, radiator |  |

| KOMATSU D355C-3 STEEL CAB Specifications |
| --- |
| EQUIPMENT WEIGHT (Additional weight to bare-tractor) | 750kg |
| DIMENSIONS: |  |
| Overall height | 4020mm |
| Ground pressure (Additional pressure to bare tractor) | 0.01kg/sq.sm |
| STEEL CAB (Window glass: double type) |  |
| Type | All steel, enclosed type |
| Weight | 750kg |
| Length | 2070mm |
| Width | 1785mm |
| Height (Floor to ceiling) | 1460mm |
| ACCESSORY: |  |
| Wiper | 2 (Front and rear) |
| Room lamp | 1 |
| Ventilator | 1 |
| Rear lamp | 2 |
| Floor mat | 1 set |
| Heater (hot water type including defroster) | 4400Kcal/hx3 |
| Inspection lamp | 1 |
| Sunvisor | 1 |
| Fog lamp | 1 |
| Fire extinguisher | 1 |
| First aid box | 1 |
| Water bottle | 1 |
| Ash tray, cigarette lighter | 1 |
| Rear view mirror | 1 |
| Double glass window | 1 set |
| Working light (for boom) | 1 |
| Winch lamp | 1 |
| Aux. Cab heater | 1,600 kcal/h x1 |
| Combustion preheater fuel tank | 8.4ltr |

| KOMATSU D355C-3 PIPELAYER LIFTING PERFORMANCE CURVE |
| --- |
| Lifting load performance curve Boom length 8560 mm |
| Wirerope for hook Diameter 20 mm |
| Wirre cutting load 27, 600 kg |
| Wirerope for boom Diameter 20 mm |
| Wirre cutting load 27, 600 kg |
| - 8 part hook line |
| - 5 part book line |
| - Weight of counterweight plate 12,900 kg - Lifting performance is shown with counterweight extended |
| BOOM OVERHANG (L) |
| KOMATSU D355C-3 PIPELAYER DRAWBAR PULL VS TRAVEL SPEED |
| Note: The drawbar pull travel speed may be subject to change depending on the graund conditions and machine weight. |
| KOMATSU D355C-3 PIPELAYER STANDARD TOOL TABLE |
| Parts No | Parts Name | Qty | Remarks |
| 09000-30006 | WRENCH | 1 SET | 8X10, 12X14, 13X17, 19X22, 24X27, 30X32 |
| 09020-10284 | SOCKET WRENCH SET | 1 SET | 10. 12. 13. 14. 17. 19. 22. 24. 27. 30. 32 |
| 09033-00190 | SCREW DRIVER | 1 |  |
| 09030-00150 | SCREW DRIVER | 1 |  |
| 09036-00150 | PLIERS | 1 |  |
| 09039-00150 | HAMMER | 1 |  |
| 09040-00800 | OILER | 1 |  |
| 07952-80001 | GREASE PUMP | 1 |  |
| 07951-11400 | NOZZLE | 1 |  |
| 09055-10390 | PINCH BAR | 1 |  |
| 09054-00009 | THICKNESS GAUGE | 1 |  |
| 08690-00265 | HYDROMETER | 1 |  |
| 195-98-11590 | SOCKET | 1 | 41 |
| 09029-00450 | PINCH BAR | 1 |  |
| 07950-90401 | CARTRIDGE | 1 |  |
| 09002-03236 | WRENCH | 1 | 32, for power line rubber hose |
| 09002-03641 | WRENCH | 1 | 36, for winch rubber hose |
| 09001-04600 | WRENCH | 2 | for winch cooler rubber hose |
| 09001-05500 | WRENCH | 2 | for power line rubber hose |
| 09019-08035 | WRENCH | 1 | for engine filter |
| 196-98-22100 | HOSE ASS’Y | 1 | For drainage of winch oil |
| 175-900-3910 | LEVER ASS’Y | 1 | For over turning fan |
| 196-98-41100 | PUMP ASS’Y | 1 | For inch-brake release |
| 09031-00100 | SCREW DRIVER | 1 |  |
| 196-98-21190 | WRENCH | 1 |  |
| 196-98-41200 | HOSE ASS’Y | 1 |  |
| 196-98-41110 | SHIM | 1 |  |
| 196-98-41151 | GASKET | 1 |  |
| 196-98-41120 | SHIM | 1 |  |
| 196-98-41161 | GASKET | 1 |  |

| KOMATSU D355C-3 PIPELAYER STANDARD SPARE PARTS TABLE |
| --- |
| PARTS No | PARTS NAME | QTY | REMARKS |
| 175-49-11850 | ELEMENT | 3 | For steering oil filter |
| 07000-43120 | O-RING | 3 | For steering oil filter |
| 175-49-11580 | ELEMENT | 3 | For transmission oil filter |
| 07000-42115 | O-RING | 3 | For transmission oil filter |
| 130-60-48210 | ELEMENT | 3 | For counterweight oil filter |
| 07000-43078 | O-RING | 3 | For counterweight oil filter |
| 144-60-11160 | ELEMENT | 3 | For winch oil filter |
| 07000-42115 | O-RING | 3 | For winch oil filter |
| 07020-0000 | FITTING | 4 |  |
| 07020-00675 | FITTING | 4 |  |
| 07020-00900 | FITTING | 4 |  |
| 600-211-1291 | CARTRIDGE | 1 | For engine oil filter |
| 600-311-7152 | CARTRIDGE | 1 | For engine fuel filter |
| 6210-11-8820 | GASKET | 6 | For cylinder head cover |
| 04122-32575 | V-BELT | 1 | For fan drive |
| 600-736-9380 | V-BELT | 1 | For alternator |
| 07002-43634 | O-RING | 1 | For torque converter oil drain |
| 07002-43634 | O-RING | 1 | For steering case oil drain |
| 07002-43634 | O-RING | 2 | For final drive case oil drain |
| 07002-44234 | O-RING | 2 | For final drive case inlet port |
| 07002-42434 | O-RING | 1 | For counterweight oil drain |
| 07002-42434 | O-RING | 2 | For winch level gauge |
| 07002-44234 | O-RING | 1 | For winch inlet port |
| 195-98-13440 | PLUG SET | 1 | For combustion heater |

| KOMATSU D355C-3 PIPELAYER ACCESSORY PARTS TABLE |
| --- |
| PARTS No | PARTS NAME | QTY | REMARKS |
| 09056-05513 | TOOL BAG | 1 |  |
|  | SPARE PARTS TABLE | 1 |  |
|  | PARTS BOOK | 1 |  |
|  | OPERATION MANUAL | 1 |  |
| 09980-10550 | OVERALL | 1 |  |
| 09982-10057 | WORK CAP | 1 |  |
|  | STARTING SWITCH KEY | 2 |  |