| “UGMK” |  |
| --- | --- |

KOMATSU HD785-5 DUMP TRUCK

WITH TIRES 27.00R49**VMTP E4 TL

- BODY ( SAE):  60М3

- ENGINE SA12V140

- FOR -40 С TO +40С TEMPERATURE

# HD785-5 DUMP TRUCK

SPECIFICATIONS

| TYPE ...................................................………………………….. | DUMP TRUCK |
| --- | --- |
| BODY CAPACITY: |  |
| STRUCK .......................................................……... | 40,0 m3 |
| HEAPED (2 : 1) ...................................................………… | 60,0 m3 |
| MAX. FROSS VEHICLE WEIGHT …………………………... | 165000 kg |

Max. gross vhicle weight not to exceed  165000 kg on 27.00 R49 ** E4 tires, including optional equipment, fuel ang payload.

| WEIGHT: |  |
| --- | --- |
| NET WEIGHT ......................................................…………….. | 66930 kg |
| DISTRIBUTION: |  |
| FRONT AXLE ...................................................……….. | 31460 kg |
| REAR AXLE .......................................................……….. | 35470 kg |
| OPERATOR ………………………………………………… | 120 kg |
| RATED PAYLOAD …………………………… | 91000 kg |
| GROSS EIGHT.....................................................…………….. | 158 010 kg |
| DISTRIBUTION: |  |
| FRONT AXLE ..................................................………... | 52140 kg |
| REAR AXLE ...................................................………….. | 105870 kg |
| PERFORMANCE: |  |
| MAX. TRAVEL SPEED ...................……….. | 65 km/hс |
| TURNING RADIUS......................................................………… | 9,9 m |
| DUMPING ANGLE ...................…….. | 480 |
| DUMPING SPEED ...............................……… | 13 second at engine rated speed |
| DIMENSION: |  |
| OVERAL LENGTH...............................................…………… | 10490 mm |
| OVERAL WIDTH....................................................………… | 5660 mm |
| OVERAL HEIGHT………………………………………….. | 5050 mm |
| WHEEL BASE........................................................................ | 4950 mm |
| TREAD: |  |
| FRONT.........................................................……... | 4230 mm |
| REAR .............................................................……... | 3500 mm |
| GROUND CLEARANCE...........................................…....….. | 810 mm |
| LOADING HEIGHT…………………………………….. | 4285 mm |
| ENGINE: |  |
| MODEL..........................................................………………… | Комацу SA12V140 |
| TYPE........................................………………………………. | WATER COOLED, 4-STROKE-CYCLE,OVERHEAD VALVE, DIRECT INJECTION TYPE, TURBOCHARGER AND AFTERCOOLER |
| No. OF CYLINDERS – BORE X STROKE...... | 12 - 140 mm x 165 mm |
| PISTON DISPLACEMENT.......................................…………. | 30,48 ltr |
| PERFORMANCE: |  |
| FLYWHEEL HORSEPOWER (GROSS) ........…………. | 783 kWT (1050 HP.) 2000 rpm |
| FLYWHEEL HORSEPOWER (NET).......…………. | 753 KWT (1010 HP.) 2000 rpm |
| MAX. TORQUE ..........................…….. | 4168 Нm (425 kgm) |
| ENGINE RPM AT MAX. TORQUE……………………… | 1400 rpm |
| FUEL SYSTEM: |  |
| FUEL………………………………………………… | DIESEL GAS OIL, ASTM SPEC. D975-60T No. 2D |
| GOVERNOR……………………………………………... | ELECTRONIC |
| LUBRICATION SYSTEM: |  |
| LUBRICATION METHOD.................……………….. | FORCED LUBRICATION |
| LUBRICATION PUMP.................……………….. | GEAR PUMP |
| LUBRICATION FILTER................……………….. | FULL-FLOW + BY-PASS |
| COOLING METHOD………...............................……… | WATER COOLED |
| COOLING METHOD ....................................………………... | FORCED CIRCULATION BY CENTRIFUGAL WATER PUMP |
| FAN TYPE…………………………………………………... | SUCTION TYPE |
| AIR CLEANER TYPE……………………………………... | DRY TYPE WITH AUTOMATIC DUST EVACUATOR AND DUST INDICATOR |
| STARTING SYSTEM: |  |
| STARTING METHOD..............................……………… | BY ELECTRIC STARTING MOTOR |
| STARTING MOTOR………………………………. | 24 V / 7.5 кWT х 2 |
| ALTERNATOR……………………………………………. | 24 V, 90 А |
| BATTERY ………………………………... | 12 V / 200 А.h х 4 |
| DAMPER: |  |
| TYPE……………………………………………………… | RUBBER TYPE |
| TORQUE CONVERTER: |  |
| MODEL……………………………………………………….. | Комацу TCA49-1A |
| TYPE………………………………………………………… | 3-ELEMENT, 2-PHASE, 1-STAGE |
| LOCK UP CLUTCH………………………………………... | WET, DOUBLE-DISC, HYDRAULICALLY CONTROLLED |
| COOLING METHOD………………………………………... | WATER COOLED |
| TRANSMISSION: |  |
| TYPE………………………………………………………... | PLANETARY GEAR AND MULTIPLE-DISC CLUTCH, ELECTRICALLY AND HYDRAULICALLY ACTUATED, FORCED LUBRICATION, FULL AUTOMATIC |
| GEAR SHIFT …………………………………………….. | 7 FORWARD AND 1 REVERCSE SPEEDS |
| GEAR RATIO: |  |
| FORWARD 1-st ………………………………………….. | 4.692 |
| 2-nd ………………………………………………………... | 3.333 |
| 3-rd…………………………………………………………. | 2.475 |
| 4-th…………………………………………………………. | 1.838 |
| 5-th…………………………………………………………. | 1.365 |
| 6-th…………………………………………………………. | 1.000 |
| 7-th…………………………………………………………. | 0.742 |
| REVERSE 1-st………………………………. …………... | 3.934 |
| DIFFERENTIAL AND REDUCTION: |  |
| TYPE………………………………………………………… | SPIRAL BEVEL GEAR, SPLASH LUBRICATION |
| REDUCTION RATIO …………………… | 3.467 |
| DIFFERENTIAL GEAR………………...……………….. | STRAIGHT BEVEL GEAR |
| FINAL DRIVE: |  |
| TYPE………………………………………………………… | PLANETARY GEAR, SPLASH LUBRICATION |
| REDUCTION RATIO………………………………………… | 6.500 |
| AXLES: |  |
| FRONT …………………………………………………….. | INDEPENDENT SUSPENSION SYSTEM |
| REAR………………………………………………………... | FULL FLOATING TYPE |
| SUAPENSION: |  |
| FRONT ……………………………………………………... | HYDROPHEUMATIC TYPE |
| REAR………………………………………………………... | HYDROPHEUMATIC TYPE |
| WHEELS: |  |
| TIRES: |  |
| FRONT ………………………………………………….. | 27.00R49**VMTP E4 TL х 2 |
| REAR …………………………………………………….. | 27.00R49**VMTP E4 TL х 4 |
| TIRE INFLATION PRESSURE: |  |
| FRONT…………………………………………………. | 686 Кpa (7,0 kg/cm2 / 100 PSI) |
| REAR …………………………………………………….. | 686 Кpa (7,0 kg/cm2 / 100 PSI) |
| STEEERING SYSTEM: |  |
| TYPE………………………………………………………… | FULL HYDROSTATIC STEERING SYSTEM WITH DOUBLE ACTING CYLINDERS |
| BRAKES: |  |
| FRONT.......................……………………………………… | AIR-OVER-HYDRAULIC, CALIPER DISC |
| REAR ..................……………………………………………. | AIR-OVER-HYDRAULIC, OIL-COOLED MULTIPLE-DISC |
| PARKING ………………………………………………….. | SPRING LOADED, CALIPER DISC |
| RETARDER……………………………..………….. | AIR-OVER-HYDRAULIC, OIL-COOLED MULTIPLE-DISC |
| CHASSIS FRAME……………………………………………... | BOX SECTION, WELDED CONSTRUCTION, LADDER TYPE |
| BODY: |  |
| TYPE………………………………………………………… | V-SHAPE, V-BOTTOM |
| INSIDE LENGTH …………………………………………… | 7480 mm |
| INSIDE WIDTH……………………….…………… | 4880 mm |
| MAX. BODY DEPTH……………………….……………. | 1930 mm |
| HYDRAULIC CONTROL UNIT: |  |
| RELIEF VALVE SETTING ……. | 20,6 Мпа (210 кг/см2 / 2.990 PSI) |
| HYDRAULIC PUMP: |  |
| LOCATION …………………………………………….. | FRONT OF TORQUE CONVERTER |
| FOR STEERING AND BODY HOIST: |  |
| TYPE…………………………………… | GEAR PUMP |
| CAPACITY …………..……………………….. | 668 ltr/min at 2100 rpm |
| FOR TORQUE CONVERTER CHARGE: |  |
| TYPE…………………………………………………… | GEAR PUMP |
| CAPACITY …………………………………………… | 353 ltr/min at 2100 rpm |
| FOR RETARDER COOLING: |  |
| TYPE…………………………………… | GEAR PUMP |
| CAPACITY …………..……………………….. | 1051 ltr/min at 2100 rpm |
| CONTROL VALVE ………………………………………... | SPOOL TYPE |
| POSITION …………………………………………… | RAISE,HOLD, FLOAT AND LOWER |
| HOIST CYLINDERS: |  |
| TYPE……………………………………………………... | 2-STAGE TELESCOPING CYLINDER, PISTON TYPE, 2-ND STAGE IS DOUBLE ACTING |
| No OF CYLINDERS- DIA х STROKE………. | 2 - (200 mm - 180 mm) х 2085 mm |
| STEERING CYLINDERS: |  |
| TYPE……………………………………………………... | DOUBLE ACTING, PISTON TYPE |
| No OF CYLINDERS- DIA х STROKE………. | 2 - 110 mm х 455 mm |
| HYDRAULIC TANK: |  |
| TYPE……………………………………………………... | EQUIPPED WITH BUILT-IN FILTERS |
| LOCATION………………………………………….. | LEFT SIDE OF FRAME |
| FILTER………………………………………………. | FULL-FLOW TYPE |
| SERVICE CAPACITY: |  |
| FUEL TANK …………………………………..…………... | 1250 ltr |
| RADIATOR………………………………..……………. | 228 ltr |
| ENGINE……………………………………..……………… | 132 ltr |
| TORQUE CONVERTER, TRANSMISSION.……………... | 102 ltr |
| DIFFERENTIAL GEAR……………………………………. | 132 ltr |
| FINAL DRIVE, EACH SIDE……………..……… | 60 ltr |
| HYDRAULIC SYSTEM: |  |
| HOIST & STEERING ..…..…… | 153 ltr |
| RETARDER COOLING ………………………..… | 246 ltr |
| SUSPENSION CYLINDERS: |  |
| FRONT ……………………………. | 20 ltr |
| REAR ……………………………….. | 17,5 ltr |

HD785-5 ТRAVEL PERFORMANCE CURVE

HD785-5 ТЯГОВЫЕ ХАРАКТЕРИСТИКИ

Экономичный режим

HD785-5 RETARDER PERFORMANCE CURVE

KOMATSU  HD785-5 DUMP TRUCK

ACCESSORY PARTS TABLE

| PART No | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
|  | STARTING SWITCH KEY | 2 |  |
|  | PARTS BOOK | 1 |  |
|  | OPERATION & MAINTENANCE MANUAL | 1 |  |

KOMATSU HD785-5  DUMP TRUCK

TOOLS TABLE

| НОМЕР ЧАСТИ | ОПИСАНИЕ | КОЛ-ВО | ПРИМЕЧАНИЕ |
| --- | --- | --- | --- |
| 09000-30006 | WRENCH | 1 |  |
| 09014-10200 | WRENCH | 1 |  |
| 09019-08035 | WRENCH | 1 | FOR FILTER |
| 09020-10284 | SOCKET WRENCH SET | 1 |  |
| 09023-00380 | HANDLE | 1 |  |
| 09033-00190 | SCREWDRIVER | 1 |  |
| 09036-00150 | PLIERS | 1 |  |
| 09039-00150 | HUMMER | 1 |  |
| 09054-00009 | THICKNESS GAUGE | 1 |  |
| 09055-10390 | BAR | 1 |  |
| 09289-10000 | GAUGE | 1 | FOR TIRES |
| 07950-90403 | CARTRIDGE | 1 |  |
| 07951-11400 | NOZZLE | 1 |  |
| 07952-80002 | GREASE PUMP | 1 |  |
| 582-98-11410 | SOCKET | 1 |  |
| 568-35-11210 | HOSE | 1 | FOR AIR |
| 281-09-11310 | AIR CONNECTOR | 1 |  |
| 281-98-12610 | PLUG | 1 |  |
| 568-35-11920 | HOSE | 1 |  |
| 04059-01080 | WIRE | 1 |  |
| 561-98-61120 | SET | 1 | FOR BRAKE DISC |
| 09056-05513 | TOOLS BAG | 1 |  |

KOMATSU HD785-5 DUMP TRUCK

SPARE PARTS TABLE

| PART No. | PART NAME | Q-TY | REMARKS |
| --- | --- | --- | --- |
| 600-211-1231 | CARTRIDGE | 4 | FOR ENGINE OIL FILTER |
| 600-212-1511 | CARTRIDGE | 2 | FOR BY-PASS FILTER |
| 07063-01210 | CARTRIDGE | 3 | FOR HYDRAULIC FILTER |
| 07000-25185 | O-RING | 3 | FOR HYDRAULIC FILTER |
| 561-60-61160 | SEAL | 3 | FOR HYDRAULIC FILTER |
| 600-311-7132 | CARTRIDGE | 2 | FOR FUEL FILTER |
| 600-411-1171 | CARTRIDGE | 2 | FOR CORROSSION RESISTOR |
| 04120-21951 | V- BELT | 1 | FOR ALTERNATOR |
| 6215-61-3690 | V- BELT | 1 | FOR FAN |
| 569-30-11600 | VALVE | 6 | FOR TIRES |
| 09284-00045 | EXTANSSION | 2 | FOR TIRES |
| 6210-11-8820 | GASKET | 12 | FOR COVER VALVES |
| 424-16-11140 | ELEMENT | 4 | FOR FILTER TRANSMISSION |
| 424-16-11130 | О-RING | 4 | FOR FILTER TRANSMISSION |
| 424-16-11630 | O-RING | 8 | FOR FILTER TRANSMISSION |
| 07002-01223 | O-RING | 4 | FOR FILTER TRANSMISSION |

KOMATSU HD785-5 DUMP TRUCK

OPTIONAL EQUIPMENT LIST

# DESCRIPTION

BATTERIES - LARGE

ALTERNATOR - 90A

27.00 R49 ** VMTP (E4) TL TIRES (BRIDGESTONE)

EXHAUST BOX + MUFFLER

RADIATOR CURTAIN

COLD WEATHER ARRANGEMENT

ELECTRONIC ENGINE OIL & COOLANT HEATER

HYDRAULIC OIL HEATER

POOR FUEL(WATER)SEPARATOR

BACK-UP LIGHT

SIDE WORKING LIGHTS

FOG LIGHTS

REAR VIEW MIRROR – RIGHT

ROPS COLUMN WITH FOPS

SEAT BELT, WIDE TYPE (78MM)

HEATER & DEFROSTOER, DOUBLE

ELECTRIC FAN

CIGA LIGHTER & ASHTRAY

DEFOGGER GLASS,FRONT

PAYLOAD METERFR (PLM-2)

BUDDY SYSTEM CUPPLER

ENGINE ROOM LIGHT

VANDALISM PROTECTION KIT

AIR DRYER

ALCOHOL INJECTOR

ENGINE SIDE COVERS

ENGINE UNDER GUARD

TRANSMISSION UNDER GUARD

PROPELLER SHAFT GUARD, FRONT

PROPELLER SHAFT GUARD, REAR

PLATFORM GUARD

TIRE GUARDS

FIRE EXTINGUISHER

FIRST AID KIT

CAP & OVERALL

GENERAL TOOL KIT

SPARE PARTS –GENERAL

AUTO GREASE (LINCOLN)

FRONT BRAKE CUT-OFF

ARSC (AUTO RETARDER SPEED CONTROL/KM)

ASR (AUTO SPIN REGULATOR)

VHMS (VEHICLE HEALTH MONITORING SYSTEM) WITHOUT ORBCOMM

FAST FILL COUPLER FOR FUEL TANK