KOMATSU WА800-3

WHEEL LOADER

WITH

11.0 m3  SPADE NOSE BUCKET WITH  TIP  TEETH

45 / 65-45-46 PR (L-5) TIRES

ROPS CANOPY & STEEL CAB

HEATER & DEFROSTER

## KOMATSU WA800-3 WHEEL LOADER

## Specifications

| OPERATING WEIGHT | 98300 kg. (216,710 lb.) |
| --- | --- |
| Operating weight includes 45 / 65-45-46PR (L-5) tubeless tires, 11.0 m3(14.4 yd3), spade nose bucket with optional tip type teeth, ROPS canopy, steel cab and operator. |
| Weight distribution (empty) |  |
| Front axle | 57300 kg (126,320 lb) |
| Rear axle | 41000 kg ( 90,390 lb) |
| FLYWHEEL HORSEPOWER: |  |
| SAE J1349 | 603 kW (808 HP) / 2000 rpm |
| DIN 6270 | 603 kW (820 PS) / 2000 rpm |
| PERFORMANCE: |  |
| Travel speed: Forward 1st 2nd 3rd Reverse 1 st 2 nd 3 rd | 7,0 km/h ( 4.3 MPH 12,3 km/h ( 7.6MPH) 28,0 km/h (17.4 MPH) 7,1 km/h (4.4MPH) 12,4 km/h (7.7 MPH) 28,3 km/h (17,6MPH) |
| Max. rimpull | 588 kN (60,000 kgf /132,280lb) |
| Turning radius: Outside corner of bucket teeth Center of outside wheel | 10940 mm ( 35' 11'' ) 9200 mm ( 30' 2'' ) |
| DIMENSIONS: |  |
| Overall length | 13730 mm ( 45' 1'' ) |
| Overall width | 4585 mm (15' 1'' ) |
| Overall height: |  |
| To top of ROPS canopy | 5275 mm ( 17' 4'' ) |
| To top of operator seat | 4460 mm ( 14' 8'' ) |
| Wheelbase | 5450 mm. ( 17' 11” ) |
| Tread, front and rear | 3350 mm ( 11' 0'' ) |
| Ground clearence | 550 mm ( 1' 10'' ) |
| LOADER PERFORMANCE: |  |
| Bucket capacity: |  |
| Heaped | 11,0 m3 ( 14,4 yd3 ) |
| Struck | 9,3 m3 ( 12,2 yd3 ) |
| Bucket width: |  |
| Cutting edge width | 4760 mm |
| Width over tire protectors | 5045 mm |
| Bucket edge | Spade nose |
| Rated load | 19800 kg ( 43,650 lb ) |
| Breakout force | 677 kN ( 69,000 kgf / 152,120 lb ) |
| Static tipping load: |  |
| Straight | 57400 kg ( 126,540 lb ) |
| Full turn | 50500 kg ( 111,330 lb ) |
| Lifting capacity: |  |
| SAE carry position | 610 kN (62,150 kgf / 137,020 lb ) |
| Max. hinge pin height | 6785 mm ( 22' 3'' ) |
| Operating height, fully raised | 9300 mm ( 30' 6'' ) |
| Dumping clearance at max. height, 45o discharge angle | 5010 mm ( 16' 5'' ) |
| Dumping reach at max. height, 45o discharge angle | 2150 mm ( 7' 1'' ) |
| Max. tilt back angle, at carry position | 50о |
| Max. dumping angle, fully raised | 50о |
| Max. digging depth below ground: |  |
| When digging angle 0о | 165 mm ( 6. 5'' ) |
| When digging angle 10о | 605 mm ( 2' 0'' ) |
| ENGINE: |  |
| Model | KOMATSU SA12V140 |
| Type | Water cooled, 4-stroke, over head valve, direct injection type, turbocharged and aftercooled diesel engine |
| No. of cylinders – bore x stroke | - 140 mm x 165 mm ( 5.51” X 6.50”) |
| Piston displacement | 30,48 ltr. (1,860 in3) |
| Performance: Rated rpm Max. torque | 2000 rpm 3727 N.m ( 380 kgf.m / 2,749 ft.lb ) at engine 1400 rpm |
| Fuel system: Fuel oil Governor | Diesel gas oil, ASTM Specifications D975-60T No.2D Electronic control |
| Lubrication system: |  |
| Lubricating method | Forced lubrication |
| Lubrication pump | Gear pump |
| Filter | Full-flow |
| Cooling method Coolingn method | Water cooled. Forced circulation by water pump |
| Air cleaner | Dry-type with automatic dust Ejector and dust indicator |
| Starting method: |  |
| Type | By electric starting motor |
| Starting motor | 2 x 7.5KW, 24V |
| Alternator | 24 V, 90A |
| Battery | 4 X 12V / 200Аh |
| TORQUE CONVERTER: |  |
| Model | KOMATSU TCА51-1A |
| Type | 3-element, single-stage and single-phase |
| Cooling method | Water cooled |
| TRANSMISSION: |  |
| Type | Powershift, planetary gear type, multiple-disc clutch, hydraulically actuated, forced lubrication |
| Gear shift | 3 forward and 3 reverse speeds |
| AXLE: |  |
| Drive system | Four-wheel drive |
| Front axle | Fixed type, full-floating |
| Rear axle | Center pin support, full-floating |
| Oscillation angle | Total 22( |
| Reduction gear | Spiral bevel gear |
| Differential gear | Straight bevel gear |
| Final drive | Planetary gear, single reduction |
| WHEELS: |  |
| Tire size | 45/65-45-46 PR (L-5) tubeless |
| Rims | 36.00 x 45 |
| Tire inflation pressure | 515 kPa (5,25 kgf/cm2/ 75 PSI) |
| BRAKES: |  |
| Service brakes | Hydraulically actuated, wet, multiple- disc brakes actuate all four wheels |
| Parking brake | Spring applied, hydraulically released, dry caliper disc brake actuates front drive shaft |
| Emergency brake | Parking brake actuates as emergency brake |
| STEERING: |  |
| Type | Frame articulation |
| Description | Fully hydraulic power steering |
| Steering angle | 40(, each side |
| HITCH: |  |
| Type | Fixed type |
| Hitch height above ground | 1390 mm ( 4' 7'' ) |
| HYDRAULIC SYSTEM: |  |
| Steering system: |  |
| Hydraulic pump | Piston pump |
| Discharge flow at rated rpm: | 307 ltr./min.( 81.1 US gal/min) |
| Relief valve setting | 31.4 Mpa ( 320 kgf /cm2 / 4,550 PSI ) |
| Control valve | Rotary valve type |
| Steering cylinder: Type | Double-acting, piston type |
| No. of cylinders – bore x stroke | 2 - 160 mm х 503 mm (6.3” x 19.8”) |
| Loader control: |  |
| Hydraulic pump | Piston pump |
| Discharge flow at rated rpm: |  |
| Loader pump | 405 ltr./min. (107.0 US gal/min) |
| Switch pump | 405 ltr./min. (107.0 US gal/min) |
| Relief valve setting | 31,4 Mpa ( 320 kgf /cm2 / 4,550 PSI ) |
| Control valve | 2-spool type |
| Control positions: |  |
| Boom spool | Raise, hold, lower and float |
| Bucket spool | Tilt-back, hold and dump |
| Valve operating method | Pressure Proportional Control (PPC) |
| PPC pump | Gear pump |
| Discharge flow at rated rpm | 68.0 ltr./min. (18.0 US gal/min) |
| Relief valve setting | 3.7 MPa ( 38 kgf /cm2 / 540 PSI ) |
| Hydraulic cylinders: |  |
| Type | Double-acting, piston type |
| No. of cylinders – bore x stroke: |  |
| Boom cylinder | 2 - 260 mm х 1368 mm (10.2” x 53.9”) |
| Bucket cylinder | 1 - 300 mm х 906 mm (11.8” x 35.7”) |
| Filter | Full-flow |
| Hydraulic cycle time: |  |
| Raise | 11,2 sec. |
| Dump | 2,0 sec. |
| Lower (empty) | 4,8 sec. |
| Total | 18,0 sec. |
| SERVICE RIFILLING CAPACITY: |  |
| Coolant | 301 ltr. ( 79.5 US gal ) |
| Fuel tank | 1425 ltr. ( 376.5 US gal ) |
| Engine | 132 ltr. ( 34.9 US gal ) |
| Torque converter) | 140 ltr. ( 37.0 US gal ) |
| Transmission ) |  |
| Front axle (differential & final drive) | 360 ltr. ( 95.1 US gal ) |
| Rear axle (differential & final drive) | 360 ltr. ( 95.1 US gal ) |
| Hydraulic system | 725 ltr.` ( 191.5 US gal ) |
| Brake system | 31 ltr. ( 8.2 US gal ) |

KOMATSU WA800-3 WHEEL LOADER

ACCESSORY PARTS TABLE

| PART NO. | PART NAME | Q' TY | REMARKS |
| --- | --- | --- | --- |
|  | PARTS BOOK | 1 |  |
|  | OPERATION & MAINTENANCE MANUAL | 1 |  |
|  | STARTING SWITCH KEY | 2 |  |

KOMATSU WA800-3 WHEEL LOADER

OPTIONAL TOOL TABLE

| PART NO. | PART NAME | Q’TY | REMARKS |
| --- | --- | --- | --- |
| 424-98-11110 | NIPPLE | 1 | For axle oil drain |
| 424-98-11120 | TUBE | 1 | For axle oil drain |
| 09000-30006 | WRENCH SET | 1 |  |
| 09020-10284 | SOCKET WRENCH SET | 1 |  |
| 09033-00190 | SCREW DRIVER | 1 |  |
| 09036-00150 | PLIERS | 1 |  |
| 09014-10200 | ADJUSTABLE WRENCH | 1 |  |
| 09001-03600 | WRENCH | 1 | 36 mm |
| 09289-00000 | GAUGE | 1 | For tire pressure |
| 07952-80003 | GREASE PUMP | 1 |  |
| 07950-90403 | CARTRIDGE (GREASE) | 1 |  |
| 07951-31400 | NOZZLE | 1 |  |
| 09019-08035 | FILTER WRENCH | 1 |  |
| 424-98-11130 | BAR | 1 |  |
| 09963-03000 | PLATE | 1 |  |
| 09054-00009 | THICKNESS GAUGE | 1 |  |
| 09989-13301 | BAG | 1 |  |
| 09056-05620 | TOOL BAG | 1 |  |

KOMATSU  WA800-3  WHEEL  LOADER

OPTIONAL SPARE PARTS TABLE

| PART NO. | PART NAME | Q' TY | REMARKS |
| --- | --- | --- | --- |
| 6210-11-8811 | GASKET | 12 | For cylinder head cover |
| 6210-11-8141 | RUBBER | 36 | For cylinder head cover |
| 600-211-1231 | CARTRIDGE | 4 | For engine oil full-flow filter |
| 600-311-7132 | CARTRIDGE | 2 | For fuel filter |
| 424-16-11140 | ELEMENT | 6 | For transmission oil filter |
| 07000-12125 | O-RING | 6 | For transmission oil filter |
| 07000-12014 | O-RING | 6 | For transmission oil filter |
| 600-212-1511 | CARTRIDGE | 1 | For engine oil bypass filter |
| 07020-00900 | FITTING | 4 |  |
| 07020-00000 | FITTING | 4 |  |
| 07020-00675 | FITTING | 4 |  |
| 20Y-60-21510 | ELEMENT | 3 | For hydraulic filter |
| 07000-12010 | O-RING | 3 | For hydraulic filter |
| 07000-15175 | O-RING | 3 | For hydraulic filter |
| 427-98-23110 | SPARE PART TABLE | 1 |  |
| 427-98-12210 | OIL | 1 | SAE 10W 10 liter |
| 427-98-12230 | GREASE | 1 | KES LM-P |
| 427-98-12240 | GREASE | 1 | KES LM-G |
| 427-98-12410 | SPRAY | 10 | Paint (Natural yellow) |
| 427-98-12420 | SPRAY | 3 | Paint (Cloud gray) |
| 09059-00800 | SPARE PARTS BOX | 1 |  |

KOMATSU WA800-3 WHEEL LOADER

OPTIONAL EQUIPMENT LIST

# DESCRIPTION

BATTERIES – LARGE

ALTERNATOR - 90A

A12V140 WITH ELECTRONIC GOVERNOR

POOR FUEL (WATER)ARRANGEMENT

SIDE WORKING LIGHT

REAR UNDER VIEW MIRROR

LIGHT, AMBER BEACON

ROLL BELT – 78 MM SUS

EMERGENCY  STEERING, AUTO, SAE

HEATER AND DEFROSTER

RADIO, AM-FM

WINDOW WASHER, REAR

PM SERVICE CONNECTOR

CAP LOCK & COVER LOCK

##### RADIATOR CORE PROTECTION  GRID

FIRE EXTENGUISHER

CAP & OVERALL

GENERAL TOOL KIT

SPARE PARTS – GENERAL

RUSSIAN PLATE

AUTO GREASING SYSTEM, LINKOLN

FAST FILL COUPLER FOR FUEL TANK, WIGGINS

POWER TRAIN U/GUARD