|  | Appendix No. to |
| --- | --- |
|  | Contract No. ÑÇÍÈ 96-01 |

KOMATSU HD1200-1

DUMP  TRUCK

LOADING CAPACITY 120 TON

Dump Body Capacity: 70m3

+400C ~ -550C Specification

With Tires 33.00-51, 50PR, type E-4 (6 pcs)

Heavy Duty Rim 24.00-51 (6 pcs)

KOMATSU HD1200 Rear Dump Truck

Specifications

Type ............................................................................................... Diesel electric drive,

Rear Dump Truck

CAPACITY:

Struck ...................................................................................       46.0 m3

Heaped (SAE 2:1)...................................................................       70.0 m3

WEIGHTS:

Empty weight .........................................................................    98,980 kg

Distribution:

Front Axle .............................................................................   46,030kg

Rear Axle ..............................................................................   52,950kg

Max. payload ..........................................................................   120,000kg

Gross weight ...........................................................................  218,980kg

Distribution:

Front Axle ............................................................................    75,620 kg

Rear Axle .............................................................................  143,360 kg

PERFORMANCE:

Max. travel speed .....................................................................  57.5 km/h

Turning radius ..........................................................................  12.5 m

Dumping angle .........................................................................  47o

Dumping speed ........................................................................  15 second

DIMENSIONS:

Overall length ...........................................................................  10,980 mm

Overall width ............................................................................    6,640 mm

Overall height

(when no load) .......................................................................   5,550 mm

Loading height

(when no load) .......................................................................   4,650 mm

Wheelbase .................................................................................  5,400 mm

Tread:

Front wheel .............................................................................  5,016 mm

Rear wheel ..............................................................................  4,100 mm

Ground clearance

(when no load)..........................................................................    780 mm

ENGINE:

Model ..........................................................................   KTA38 C-1200

Type ............................................................................   Water cooled 4 cycle,

V-type,  direct injection,

turbocharged and aftercooled

No. of cylinder

bore x stroke ..............................................................  12-159mm x 159mm

Piston displacement .......................................................  37.8 litter

Performance:

Rated brake horse power ............................................    895 kw/2,100 RPM

(1,200 HP/2,100 RPM)

Flywheel horse power ..................................................   865 kw/2,100 RPM

(1,160 HP/2,100 RPM)

Max. torque .................................................................   4,678 Nm/1,300 RPM

(476 kgm/1,300 RPM)

Lubrication system:

Lubricating method .......................................................  Gear pump, forced lubrication

Filter ............................................................................  Full flow type and by-pass type

Oil cooler .....................................................................  Water cooled

Cooling system .............................................................…  Forced circulation by  water

pump, suction type fan

Starting method ..................................................…........... Air starting motor

Attached equipment:

Air compressor ............................................................. two cylinder (850 l/min)

Electric equipment ........................................................ 24 volt alternator system

with 75 amperes

Engine mounting ................................................................ Front trunion support

Radiator mounting

Flywheel and flywheel housing

PT Pump

Oil Pan .............................................................................  Center sump, 129 litter capacity

Full flow filter and by-pass filter

ELECTRIC DRIVE SYSTEM:

Type ..................................................................................   AC/DC current

Alternator............................................................................   TOYO ELECTRIC MFG.

Brushless type alternator

with built-in exciter,

model TDK-6620B

connected to the engine

through flexible coupling.

Rated 809 kW Input for

traction.

Traction motor ..................................................................…  TOYO ELECTRIC MFG.

Series wound DC motor,

model TDK-8911D. Rated

output is 343 kW/motor

Cooling ...............................................................................   Forced, filtered air cools

both traction motors and

alternator

FINAL DRIVE:

Type ...................................................................................   Planetary gear

Axle ....................................................................................   Heavy duty, full floating

Reduction ratio ....................................................................   29.37 : 1

STEERING SYSTEM: .......................................................................   Full hydraulic power

steering with dual

steering   cylinder

TIRES:

Front and rear .....................................................................   33.00-51, 50 PR, type E-4

tread, tubeless,

front x 2, rear x 4.

Rim .....................................................................................   24.00-51

BRAKES:

Emergency and parking ........................................................  Spring loaded,

calliper disk-type.

Service, front  and rear .........................................................  Brake-drum shoe internal -

expanding type with

hydropneumatic drive,

980 x 250 mm

Dynamic brake ................................................................    1492 kW  (2000 HP) (See

performance curve) Dynamic

braking on rear wheel,

utilises wheel motors as

generators and dissipates

vehicle kinetic energy

into air cooled resistors.

SUSPENSIONS, front and rear ....................................................    hydropneumatic type

DUMP SYSTEM:

Type ...............................................................................    Twin, 3-stage hydraulic

cylinder double acting in

third stage.

Hydraulic pump:

Type ................................................................................…    Gear pump

Max. pressure .....................................................................    210 kg/cm2

Capacity ...........................................................................…   660 ltr/min

CAPACITY:

Fuel tank ...............................................................................  1,900 ltr.

Cooling water .........................................................................    250 ltr.

Engine oil ...............................................................................    134 ltr.

CAB ...........................................................................................  One side cab type.

Steering wheel is located

on the left side. One

operator seat and one

auxiliary seat.

DUMP BODY ..............................................................................   SAE Geometric capacity of

rock type body is 46,0 m3

and with heap - 70 m3.

The thickness of bottom

of the body is 19 mm and

tensile strength of bottom plate

is 130 kg/mm2.