KOMATSU HD1200 Rear Dump Truck

Specifications

| Type ………………………………..……………………… | Diesel electric drive, Rear Dump Truck |
| --- | --- |
| CAPACITY: |
|  | Struck …………………………………..……………. | 46.0 m3 |
| Heaped (SAE 2:1) …………………..…………….. | 70.0 m3 |
| WEIGHTS: |
|  | Empty weight ………………………..……………… | 98,980 kg |
| Distribution: |
|  | Front Axle …………………..…………………… | 46,030 kg |
| Rear Axle ………………………………………… | 52,950 kg |
| Max. payload ……………………………………….. | 120,000 kg |
| Gross weight ………………………………………… | 218,980 kg |
| Distribution: |
|  | Front Axle ……………………………………….. | 75,620 kg |
| Rear Axle ………………………………………… | 143,360 kg |
| PERFORMANCE: |
|  | Max. travel speed ………………………………….. | 57.5 km/h |
| Turning radius ………………………………………. | 12.5 m |
| Dumping angle ……………………………………… | 47.0 deg. |
| Dumping speed …………………………………….. | 15 second |
| DIMENSIONS: |
|  | Overall length ……………………………………….. | 10,980 mm |
| Overall width ………………………………………… | 6,640 mm |
| Overall height |
|  | (when no load) ………………………………… | 5,550 mm |
| Loading height |
|  | (when no load) ………………………………… | 4,650 mm |
| Wheelbase …………………………………………… | 5,400 mm |
| Tread: |
|  | Front wheel …………………………………….. | 5,016 mm |
| Rear wheel ……………………………………… | 4,100 mm |
| Ground clearance |
|  | (when no load)…………………………………. | 780 mm |
|  | ENGINE: |
|  | Model ………………………………………………… | KTA38 C-1200 |
| Type ………………………………………………… | Water cooled 4 cycle, V-type, direct injection, turbocharged and aftercooled |
| No. of cylinder |
|  | bore x stroke ………………………………………… | 12-159mm x 159mm |
| Piston displacement ………………………………. | 37.8 litter |
| Performance: |
|  | Rated brake horse power ……………………… | 895 kw/2,100 RPM |
|  | (1,200 HP/2,100 RPM) |
| Flywheel horse power …………………………….. | 865 kw/2,100 RPM |
|  | (1,160 HP/2,100 RPM) |
| Max. torque …………………………………………. | 4,678 Nm/1,300 RPM |
|  | (476 kgm/1,300 RPM) |
| Lubrication system: |
|  | Lubricating method ……………………………… | Gear pump, forced lubrication |
| Filter …………………………………………………… | Full flow type and by-pass type |
| Oil cooler …………………………………………….. | Water cooled |
| Cooling system …………………………………….. | Forced circulation by water pump, suction type fan |
| Starting method ……………………………………. | Air starting motor |
| Attached equipment: |
|  | Air compressor ……………………………………… | two cylinder (850 l/min) |
| Electric equipment ………………………………… | 24 volt alternator system with 75 amperes |
| Engine mounting …………………………………… | Front trunion support |
| Radiator mounting |

Flywheel and flywheel

| housing |
| --- |
|  | PT Pump |
|  | Oil Pan ………………………………………………… | Center sump, 129 litter capacity |
| Full flow filter and by-pass filter |
| ELECTRIC DRIVE SYSTEM: |
|  | Type …………………………………………………… | AC/DC current |
| Alternator …………………………………………….. | TOYO ELECTRIC MFG. Brushless type alternator with built-in exciter, model TDK-6620B connected to the engine through flexible coupling. Rated 809 kW Input for traction. |
| Traction motor ……………………………………… | TOYO ELECTRIC MFG. Series wound DC motor, model TDK-8911D. Rated output is 343 kW/motor |
| Cooling ……………………………………………….. | Forced, filtered air cools both traction motors and alternator |
| FINAL DRIVE: |
|  | Type …………………………………………………… | Planetary gear |
| Axle …………………………………………………… | Heavy duty, full floating |
| Reduction ratio …………………………………….. | 29.37 : 1 |
| STEERING SYSTEM: | Full hydraulic power steering with dual steering cylinder |
| TIRES: |
|  | Front and rear ………………………………………. |

33.00-51, 50 PR, type E-4 tread, tubeless,

| front x 2, rear x 4. |
| --- |
| Rim …………………………………………………….. | 24.00-51 |
| BRAKES: |
|  | Emergency and parking ………………………….. | Spring loaded, calliper disk-type. |
| Service, front and rear ……………………………. | Brake-drum shoe internal - expanding type with hydropneumatic drive, 980 x 250 mm |
| Dynamic brake ……………………………………… | 1492 kW (2000 HP) (See performance curve) Dynamic braking on rear wheel, utilises wheel motors as generators and dissipates vehicle kinetic energy into air cooled resistors. |
| SUSPENSIONS, front and rear ……………………… | hydropneumatic type |
| DUMP SYSTEM: |
|  | Type …………………………………………………… | Twin, 3-stage hydraulic cylinder double acting in third stage. |
| Hydraulic pump: |
|  | Type ………………………………………………. | Gear pump |
| Max. pressure …………………………………. | 210 kg/cm2 |
| Capacity …………………………………………. | 660 ltr/min |
| CAPACITY: |
|  | Fuel tank ………………………………………… | 1,900 ltr. |
| Cooling water ………………………………….. | 250 ltr. |
| Engine oil ……………………………………… | 134 ltr. |
| CAB ………………………………………………………… | One side cab type. Steering wheel is located on the left side. One operator seat and one auxiliary seat. |
| DUMP BODY …………………………………………… | SAE Geometric capacity of rock type body is 46.0 m3 and with heap - 70 m3. The thickness of bottom of the body is 19 mm and tensile strength of bottom plate is130 kg/mm2. |