KOMATSU HD1200-1

DUMP TRUCK

LOADING CAPACITY 120 TON

1. Dump Body Capacity: 70 m3

2. -30oC ~ +40oC  Specification

3. With KTTA38C-1350 Engine

4. Without Tires

5. Without Vessel

# KOMATSU HD1200-1 Rear Dump Truck

## Specifications

Type .........................................................................…………….   Diesel electric drive,

Rear Dump Truck

CAPACITY:

Struck ...........................................................…………….        46.1 m3

Heaped (SAE 2:1)............................................................        70.0 m3

WEIGHTS:

Empty weight ...................................................................     98,660 kg

Distribution:

Front Axle .....................................................................     45,930 kg

Rear Axle ......................................................................     52,730 kg

Max. payload ....................................................................   120,000 kg

Gross weight ...................................................……………  218,660 kg

Distribution:

Front Axle ........................................................................  75,510 kg

Rear Axle ........................................................................ 143,150 kg

PERFORMANCE:

Max. travel speed ...............................................................   57.5 km/h

Turning radius .........................................................….....…  12.5 m

Dumping angle ............................................................……   47.0o

Dumping speed ................................................................… 15 second

DIMENSIONS:

Overall length .....................................................................  10,980 mm

Overall width .......................................................................   6,640 mm

Overall height

(when no load) .................................................……..........  5,560 mm

Loading height

(when no load) ...............................................................…. 4,650 mm

Wheel base .........................................................................   5,400 mm

Tread:

Front wheel ......................................................................   5,016 mm

Rear wheel ......................................................................    4,100 mm

Ground clearance

(when no load)....................................................................    780 mm

ENGINE:

Model ................................................................................. KTTA38C-1350

Type ..................................................................................  Water cooled 4 cycle,

V-type,  direct injection,

turbocharged and aftercooled

No. of cylinder-

bore x stroke ..................................................................  12-159mm x 159mm

Piston displacement ..........................................................  37.8 litres

Performance:

Rated brake horse power ................................................  1,007 kw/2,100 RPM

(1,350 HP/2,100 RPM)

Flywheel horse power .....................................................     977 kw/2,100 RPM

(1,310 HP/2,100 RPM)

Max. torque ....................................................................   5,264 Nm/1,500 RPM

(536,8 kgm/1,500 RPM)

Lubrication system:

Lubricating method .........................................................  Gear pump, forced lubrication

Filter ..............................................................................   Full flow type and by-pass type

Oil cooler .......................................................................   Water-cooled

Cooling system .................................................................   Forced circulation by

water pump,

suction type fan

Starting method .............................................................…   Air starting motor

Attached equipment:

Air compressor ...........................................................….  Two cylinder (850 l/min)

Electric equipment ......................................................….  24 volt alternator system

with 75 amperes

Engine mounting ..............................................................…..  Front trunion support

Radiator mounting

Flywheel and flywheel housing

PT Pump

Oil Pan ...........................................................................…… Center sump,

129 litres capacity

Full flow filter and by-pass filter

ELECTRIC DRIVE SYSTEM:

Type ..................................................................................  AC/DC current

Alternator...........................................................................   TOYO ELECTRIC MFG.

Brushless type alternator

with built-in exciter,

model TDK-6620B connected

to the engine through

flexible coupling. Rated

809 kW Input for traction.

Traction motor ...................................................................  TOYO ELECTRIC MFG.

Series wound DC motor,

model TDK-8911D. Rated

output is 343 kW/motor

Cooling ............................................................................... Forced, filtered air cools

both traction motors and

alternator

FINAL DRIVE:

Type ................................................................................... Planetary gear

Axle .................................................................................... Heavy duty, full floating

Reduction ratio ................................................................... 29.37 : 1

STEERING SYSTEM: .................................................................... Full hydraulic power

steering with dual

steering   cylinder

TIRES:

Front and rear .................................................................... 33.00-51, 50 PR, type E-4

tread, tubeless,

front x 2, rear x 4.

(without tires)

Rim ...................................................................................  24.00-51

Heavy Duty Rim (for Radial Tires)

BRAKES:

Emergency and parking ....................................................  Spring loaded, caliper

Disc type.

Service, front and rear .......................................................  Brake-drum shoe internal -

expanding type with

hydropneumatic drive,

980 x 250 mm

Dynamic brake ..................................................................  1492 kW  (2000 HP) (See

performance curve) Dynamic

braking on rear wheel,

utilizes wheel motors as

generators and dissipates

vehicle kinetic energy

into air cooled resistors.

SUSPENSIONS, front and rear ....................................................  hydropneumatic type

DUMP SYSTEM:

Type .................................................................................. Twin, 3-stage hydraulic

cylinder double acting in

third stage.

Hydraulic pump:

Type .....................................................................................   Gear pump

Max. pressure ......................................................................   210 kg/cm2

Capacity ...............................................................................   660 ltr/min

CAPACITY:

Fuel tank ................................................................................   1,900 ltr.

Cooling water .........................................................................      250 ltr.

Engine oil ...............................................................................      134 ltr.

CAB ...........................................................................................    One side cab type.

Steering wheel is located

on the left side. One

operator seat and one

auxiliary seat.

DUMP BODY ..............................................................................   SAE Geometric capacity of

rock type body is 46.1 m3

and with heap - 70 m3.

The thickness of bottom

of the body is 19 mm and

tensile strength of bottom plate

is 130 kg/mm2.

(without Vessel)

HD1200 GRADEABILITY / SPEED / RIMPULL

GROSS VEHICLE WEIGHT  (kg x 1000)

HD1200 DYNAMIC BRAKING PERFORMANCE

GROSS VEHICLE WEIGHT (kg x 1000)

1) STANDARD EQUIPMENT

1-1) Cab:

Ash tray

Cigar lighter

Dome light

Adjustable sun visor

Low air pressure alarm

Central warning light

Windshield wiper

Windwasher tank

Glove box

Heater & defroster

1-2) Instrument:

Engine oil temperature gauge

Engine water temperature gauge

Speed meter (km/h)

Tachometer

Air pressure gauge

Voltmeter (Battery out-put)

Hourmeter

Fuel gauge

Engine oil pressure indicator light

Engine water temperature indicator light

Over speed warning light

Dynamic brake indicator light

Service brake indicator light

Air pressure warning light

High beam indicator light

Brake lock indicator light

Parking brake indicator light

Turning signal indicator light

Electric equipment over heat warning light

Ground fault indicator light

Air cleaner restriction gauge

Lamp test switch

Hubodometer

Lamp switch (head light/instrument panel light/

Tail light)

Working light switch

Wiper switch

Parking brake switch

Brake lock switch

Fuel gauge on tank

1-3) Vehicle

Dynamic retarding light

Backup light

Stop light

Tail light

Front clearance light (white) and

turn signal light (yellow)

Rear turn signal light (yellow)

Working light

Dome light (for engine room)

Dome light (for axle housing)

1-4) Safety equipment:

Horn (warning)

Backup warning horn

Mirrors LH and RH

Air-over-hydraulic service brake with emergency relay

Parking brake

Full time power steering

Wheel brake lock

Radiator fan guard

Operator seat belt

Propulsion interlock   (Parking brake/Control box door

open/Electric equipment heater

switch on/Brake lock)

Safety guard on bonnet

Safety guard for P.D.U.

2) SPECIALLY ATTACHED EQUIPMENT

- Extended range dynamic retarding

- Pull-hook (Rear)

- Pull-hook (Front)

- Low insulation lamp

- Rear clearance light (red)

- Reinforced operator seat

- Engine oil temperature gauge

- Engine oil pressure gauge

- Dump lever indicator light and sound signalization

- Preliminary fuel pumping system

- Socket for portable inspection lamp

(24V Russian Standard)

- Alcohol injection device

- Traction motor preheating device

- Traction motor preheating switch

- Air dryer

- Winter-proof hoses, wiring and shields

- Pre-lubrication device

- Group lubrication system (2 groups: hoist cylinder

pin upper and lower, body hinge pin

- LINCOLN centro-matic system

for 2 points lubrication

- Radiator coolant level warning device

with caution lamp and sound signal in cabin

- Emergency steering system

- Propulsion interlock (Body-up)

- Ladder to fuel tank

- Reinforced bumper

- Automatic emergency engine stopper

- High pressure line-filter

- Passenger seat

- Anti-slip plate on bonnet

- Hydraulic oil temperature gauge with warning lamp

- Radiator shutter (thermostatically controlled)

- Clearance light

- Air conditioner

- One spare heavy duty rim (for radial tires)

- Platform guard (R.H.)

- PLM System (Printer-type)

3) STANDARD TOOLS:

09000-30006            Open end wrench set

09002-00810            wrench

09002-01214            wrench

09002-01317            wrench

09002-01922            wrench

09002-02427            wrench

09002-03032            wrench

09007-00528            wrench

09007-00632            wrench

09007-00836            wrench

09014-10200            wrench

09020-10284            Socket wrench set

09021-01016            socket

09021-01319            socket

09021-01422            socket

09021-01725            socket

09021-01928            socket

09021-02233            socket

09021-02436            socket

09021-02739            socket

09021-03044            socket

09021-03246            socket

09021-03653            socket

09022-00150            extension

09022-00250            extension

09023-00300            handle

09024-00300            handle

09025-00075            joint

09026-00250            handle

09027-00300            bar

09031-00100            driver, screw

09031-00150            driver, screw

09036-00150            pliers

09039-00150            hammer

09054-00009            gauge, thickness

09055-10390            bar

09289-10000            gauge, tire

07950-10400            pump, grease

07951-21045            nozzle A

07951-11450            nozzle B

07950-90403            cartridge, grease

09023-00380            handle

178-98-11120           socket

581-98-12120           adapter, handle

09288-20011            hose

09285-00000            adapter

09019-08035            wrench

287-98-12110           wrench

09084-00915            socket

09084-01118            socket

09084-01220            socket

09084-01422            socket

09084-01524            socket

09084-02030            socket

09082-01719            wrench

09082-01214            wrench

09056-05513            bag

6721-01-7501           drain hose ass'y

OTHER ATTACHED ARTICLES

One each of key for driver's door key

and starting key

One set of manuals