### KOMATSU HD1200-1

DUMP TRUCK

- Rated payload: 125 ton

- Dump Body Capacity: 81 m3

- Heavy Duty Rim 24.00-51 (6 pcs.)

- KTTA38C-1350 Engine

- +40oC ~ -60oC  Specification

- Cabin ROPS

# KOMATSU HD1200-1 Rear Dump Truck

## Specifications

Type .........................................................................…………….   Diesel electric drive,

Rear Dump Truck

CAPACITY:

Struck ...........................................................…………….        56.3 m3

Heaped (SAE 2:1)............................................................        81.0 m3

WEIGHTS:

Empty weight ...................................................................    100,880 kg

Distribution:

Front Axle .....................................................................     46,730 kg

Rear Axle ......................................................................     54,150 kg

Rated payload ………………………………………………..    125,000 kg

Max. payload ....................................................................   136,000 kg

Gross weight ...................................................……………  225,880 kg

Distribution:

Front Axle ........................................................................  77,800 kg

Rear Axle ........................................................................ 148,080 kg

PERFORMANCE:

Max. travel speed ...............................................................   57.5 km/h

Turning radius .........................................................….....…  12.5 m

Dumping angle ............................................................……   47.5o

Dumping speed ................................................................… 15 second

DIMENSIONS:

Overall length .....................................................................  10,980 mm

Overall width .......................................................................   6,640 mm

Overall height

(when no load) .................................................……..........  5,560 mm

Loading height

(when no load) ...............................................................…. 4,925 mm

Wheel base .........................................................................   5,400 mm

Tread:

Front wheel ......................................................................   5,016 mm

Rear wheel ......................................................................    4,100 mm

Ground clearance

(when no load)....................................................................    780 mm

ENGINE:

Model ................................................................................. KTTA38C-1350

Type ..................................................................................  Water cooled 4 cycle,

V-type,  direct injection,

turbocharged and aftercooled

No. of cylinder-

bore x stroke ..................................................................  12-159mm x 159mm

Piston displacement ..........................................................  37.8 litres

Performance:

Rated brake horse power ................................................  1,007 kw/2,100 RPM

(1,350 HP/2,100 RPM)

Flywheel horse power .....................................................     977 kw/2,100 RPM

(1,310 HP/2,100 RPM)

Max. torque ....................................................................   5,264 Nm/1,500 RPM

(536,8 kgm/1,500 RPM)

Lubrication system:

Lubricating method .........................................................  Gear pump, forced lubrication

Filter ..............................................................................   Full flow type and by-pass type

Oil cooler .......................................................................   Water-cooled

Cooling system .................................................................   Forced circulation by

water pump,

suction type fan

Starting method .............................................................…   Air starting motor

Attached equipment:

Air compressor ...........................................................….  Two cylinder (850 l/min)

Electric equipment ......................................................….  24 volt alternator system

with 75 amperes

Engine mounting ..............................................................…..  Front trunion support

Radiator mounting

Flywheel and flywheel housing

PT Pump

Oil Pan ...........................................................................…… Center sump,

129 litres capacity

Full flow filter and by-pass filter

ELECTRIC DRIVE SYSTEM:

Type ..................................................................................  AC/DC current

Alternator...........................................................................   TOYO ELECTRIC MFG.

Brushless type alternator

with built-in exciter,

model TDK-6620B connected

to the engine through

flexible coupling. Rated

809 kW Input for traction.

Traction motor ...................................................................  TOYO ELECTRIC MFG.

Series wound DC motor,

model TDK-8911D. Rated

output is 343 kW/motor

Cooling ............................................................................... Forced, filtered air cools

both traction motors and

alternator

FINAL DRIVE:

Type ................................................................................... Planetary gear

Axle .................................................................................... Heavy duty, full floating

Reduction ratio ................................................................... 29.37 : 1

STEERING SYSTEM: .................................................................... Full hydraulic power

steering with dual

steering   cylinder

TIRES:

Front and rear .................................................................... 33.00R51 ((, VRLS

(not included in supply scope /                                            tubeless,

to be supplied separately)                                                  front x 2, rear x 4.

Rim ...................................................................................  24.00-51

Heavy Duty Rim (for Radial Tires)

BRAKES:

Emergency and parking ....................................................  Spring loaded, caliper

Disc type.

Service, front and rear .......................................................  Brake-drum shoe internal -

expanding type with

hydropneumatic drive,

980 x 250 mm

Dynamic brake ..................................................................  1492 kW  (2000 HP) (See

performance curve) Dynamic

braking on rear wheel,

utilizes wheel motors as

generators and dissipates

vehicle kinetic energy

into air cooled resistors.

SUSPENSIONS, front and rear ....................................................  hydropneumatic type

DUMP SYSTEM:

Type .................................................................................. Twin, 3-stage hydraulic

cylinder double acting in

third stage.

Hydraulic pump:

Type .....................................................................................   Gear pump

Max. pressure ......................................................................   210 kg/cm2

Capacity ...............................................................................   660 ltr/min

CAPACITY:

Fuel tank ................................................................................   1,900 ltr.

Cooling water .........................................................................      250 ltr.

Engine oil ...............................................................................      134 ltr.

CAB ...........................................................................................    One side cab ROPS type.

Steering wheel is located

on the left side. One

operator seat and one

auxiliary seat.

DUMP BODY ..............................................................................   SAE Geometric capacity of

rock type body is 56.3 m3

and with heap - 81 m3.

The thickness of bottom

of the body is 19 mm and

tensile strength of bottom plate

is 130 kg/mm2.

**

| - Max. noise level in cabin of Dump Truck (at full stop) at operator’s head level at the time of delivery | 87 dB (A) |
| --- | --- |
| - Max. vibration level in cabin of Dump Truck (at full stop) at the time of delivery: |  |
| at steering wheel | 106 dB |
| at operator’s seat | 104 dB |
| at pedals | 100 dB |
| - Max. contents of exhaust gasses (at full stop, at the time of delivery): |  |
| CO | 50 ppm |
| CH (HC) | 200 ppm |
| NOx | 4000 ppm |

* Above mentioned data is taken by KOMATSU’s measuring method.

#### HD1200 GRADEABILITY / SPEED / RIMPULL

GROSS VEHICLE WEIGHT  (kg x 1000)

HD1200 DYNAMIC BRAKING PERFORMANCE

GROSS VEHICLE WEIGHT (kg x 1000)

1) STANDARD EQUIPMENT

1-1) Cab:

Ash tray

Cigar lighter

Dome light

Adjustable sun visor

Low air pressure alarm

Central warning light

Windshield wiper

Windwasher tank

Glove box

Heater & defroster (4,400 kcal/h)

1-2) Instrument:

Engine oil temperature gauge

Engine water temperature gauge

Speed meter (km/h)

Tachometer

Air pressure gauge

Voltmeter (Battery out-put)

Hourmeter

Fuel gauge

Engine oil pressure indicator light

Engine water temperature indicator light

Over speed warning light

Dynamic brake indicator light

Service brake indicator light

Air pressure warning light

High beam indicator light

Brake lock indicator light

Parking brake indicator light

Turning signal indicator light

Electric equipment over heat warning light

Ground fault indicator light

Air cleaner restriction gauge

Lamp test switch

Hubodometer

Lamp switch (head light/instrument panel light/

Tail light)

Working light switch

Wiper switch

Parking brake switch

Brake lock switch

Fuel gauge on tank

1-3) Vehicle

Dynamic retarding light

Backup light

Stop light

Tail light

Front clearance light (white) and

turn signal light (yellow)

Rear turn signal light (yellow)

Working light

Dome light (for engine room, LH)

Dome light (for axle housing)

1-4) Safety equipment:

Horn (warning)

Backup warning horn

Mirrors LH and RH

Air-over-hydraulic service brake with emergency relay

Parking brake

Full time power steering

Wheel brake lock

Radiator fan guard

Operator seat belt

Propulsion interlock   (Parking brake/Control box door

open/Electric equipment heater

switch on/Brake lock)

Safety guard on bonnet

Safety guard for P.D.U.

2-1) SPECIALLY ATTACHED EQUIPMENTS

- Extended range dynamic retarding

- Fire extinguishing system (covering engine/ generator/ hydraulic pumps, including PDU; switch on of this system effected in the cabin and on the ground) – 3 bottles.

- Pull-hook (Rear)

- Low insulation lamp

- Rear clearance light (red)

- Reinforced operator seat

- Engine oil temperature gauge

- Dump lever indicator light and sound signalization

- ( Preliminary fuel pumping system

- Socket for portable inspection lamp (24V Russian Standard)

- ( Traction motor preheating device with switch

- ( Fuel fired heater (“MIKUNI” model M-135, 13500 Kcal/h, air flow 750 m3/h).

Heater for Cab/Electric control box/battery box/air equipment box

- ( Engine side cover

- ( Engine room undercover

- ( Engine winter-proof intake system

- ( Alcohol injection device

- ( Air dryer with heater

- ( Winter-proof hoses, wiring and shields

- ( 2 units of heavy duty additional car heater with switch (4400 kcal)

- Pre-lubrication device

- Ground lubrication system (2 groups, hoist cylinder pin upper and lower, body hinge pin)

- LINCOLN centro-matic system for 8 points lubrication

- Radiator coolant level warning device with caution lamp and sound signal in cabin

2-2) SPECIALLY ATTACHED EQUIPMENTS

- Emergency steering system

- Propulsion interlock (Body-up)

- Ladder to fuel tank

- Reinforced bumper

- Automatic emergency engine stopper

2-3) OPTIONAL EQUIPMENTS

- Hydraulic oil temperature gauge with warning lamp

- High pressure line-filter

- Passenger seat

- Halogen lamp head light assembly with H1 bulb x 2 psc

- Halogen lamp head light assembly with H4 bulb x 2 psc

- Hydraulic circuit supposable hydraulic pressure from outside (couple type)

- ( Radiator shutter (thermostatically controlled)

- Platform guard (R.H.)

- Spot fog lamp (H3) with switch

- Anti-slip plate on bonnet

- Strengthened type body rear rib

- Body wear plate Type B

- Heavy-duty rim instead of standard rim

- ROPS cabin

- ( Radiator curtain

- Mirror (RH) mud guard

- ( Heated mirror (RH & LH)

- Fuel tank quick charge (WIGGINS)

- ( Electrical heater for engine oil and coolant (AC 230V)

- ( Electrical heater for hydraulic oil and PDU

- ( Fuel tank strainer relocation

- PLM System (PC-type)

( marked is for – 60oC equipments

3) STANDARD TOOLS:

| 09000-30006 | wrench set |
| --- | --- |
| 09007-00528 | wrench |
| 09007-00632 | wrench |
| 09007-00836 | wrench |
| 09014-10200 | wrench |
| 09020-10284 | socket wrench |
| 09031-00100 | screw, driver |
| 09031-00150 | screw, driver |
| 09036-00150 | pliers |
| 09039-00150 | hammer |
| 09054-00009 | gauge |
| 09055-10390 | bar. pinch |
| 09289-10000 | gauge |
| 07952-80002 | pump assembly |
| 07951-11400 | nozzle |
| 07950-90403 | cartridge |
| 09023-00380 | handle |
| 178-98-11120 | socket |
| 581-98-12120 | adapter |
| 09288-20011 | hose |
| 09285-00000 | adapter |
| 09019-08035 | wrench |
| 287-98-12110 | wrench |
| 09084-00915 | socket |
| 09084-01118 | socket |
| 09084-01220 | socket |
| 09084-01422 | socket |
| 09084-01524 | socket |
| 09084-02030 | socket |
| 09082-01719 | wrench |
| 6721-01-7501 | hose assembly |
| 09056-05513 | bag |

| OTHER ATTACHED ARTICLES | One each of key for driver's door key and starting key One set of manuals |
| --- | --- |

| THE BUYERS | THE SELLERS | THE WITNESS |
| --- | --- | --- |
| ____________________ | ______________________ | ______________________ |